Initial Environmental Examination

TA 8068-KAZ June 2012

KAZ: Central Asia Regional Economic Cooperation (CAREC) Corridor 3 (Shymkent-Tashkent Road) Rehabilitation Project (Road Section Km 705–742)

Prepared by Madina J  unussova for the Ministry of Transport and Communications and t	he

Asian Development Bank.

TA-8068 (KAZ) CAREC Transport Corridor 3	SHYMKENT - TASHKENT ROAD REHABILITATION PROJECT

Ministry of Transport and Communications (MOTC) Republic of Kazakhstan

DRAFT

INITIAL ENVIRONMENTAL EXAMINATION REPORT

for

TA-8068 (KAZ)

Central Asia Regional Economic Cooperation (CAREC) Transport Corridor 3

SHYMKENT - TASHKENT ROAD REHABILITATION PROJECT ROAD SECTION KM 705 - 742

Prepared by

Madina Junussova, National Environmental Consultant

June 2012

Table of Content

EXECUTIVE SUMMARY .............................................................................................................. 6

1 Introduction ............................................................................................................................ 6

2 Description of the Environment.............................................................................................. 6

3 Anticipated Environmental Impacts / Mitigation Measures and EMP .................................... 7

4 Conclusion and Recommendations ....................................................................................... 7

A. INTRODUCTION ...................................................................................................................... 8

A.1 Project Background and Objective of the Study ................................................................. 8

A.2 Methodology and Scope of the Study ................................................................................ 8

A.3 Study Area.......................................................................................................................... 9

B. POLICY, LEGAL, AND ADMINISTRATIVE FRAMEWORK ................................................... 10

B.1 Kazakhstan Government Environmental Laws, Regulations and Guidelines .................. 10

B.2 Asian Development Bank (ADB) Environmental Policies and Guidelines ........................ 13

B.3 Administrative Framework ................................................................................................ 13

C. DESCRIPTION OF THE PROJECT....................................................................................... 15

C.1 Main Technical Features .................................................................................................. 15

C.2 Traffic Forecast ................................................................................................................ 20

D. ANALYSIS OF ALTERNATIVES............................................................................................ 21

D.1 "No-Project" Option .......................................................................................................... 21

D.2 Design Alternatives .......................................................................................................... 21

E. DESCRIPTION OF THE ENVIRONMENT (BASELINE DATA) ............................................. 23

E.1 Ecological Environment .................................................................................................... 23

E.1.2 Flora (Vegetation and Plant Species)........................................................................ 23

E.1.3 Sensitive Habitats & Protected Areas........................................................................ 24

E.2 Physical Environment ....................................................................................................... 24

E.2.1 Geologic Characteristics & Resources ...................................................................... 25

E.2.2 Soil Characteristics.................................................................................................... 25

E.2.3 Soil Quality ................................................................................................................ 26

E.2.4 Hydrology .................................................................................................................. 27

E.2.5 Water Quality............................................................................................................. 27

E.2.6 Groundwater.............................................................................................................. 27

E.2.7 Air Quality .................................................................................................................. 28

E.2.8 Climatic Context ........................................................................................................ 28

E.3 Social and Economic Environment................................................................................... 30

E.3.1 Administrative Organization....................................................................................... 30

E.3.2 Economic Resources ................................................................................................ 30

E.3.3 Transport Infrastructure ............................................................................................. 31

E.3.4 Water Supply & Irrigation Systems............................................................................ 31

E.3.5 Wastewater & Solid Waste Disposal ......................................................................... 31

E.3.6 Electrical Power, Pipelines & Other Utilities .............................................................. 32

E.3.7 Land Uses and Displacement Issues ........................................................................ 32

E.3.8 Demographic Characteristics .................................................................................... 32

E.3.9 Employment .............................................................................................................. 32

E.3.10 Employment 	Ethnic & Vulnerable Groups ............................................................ 33

E.3.11 Health Facilities and Public Health Issues............................................................... 33

E.3.12 Local Education Facilities and Amenities ................................................................ 34

E.3.13 Human Trafficking ................................................................................................... 34

E.3.14 Cultural Resources .................................................................................................. 35

E.3.15 Public Safety ........................................................................................................... 35

F. ANTICIPATED ENVIRONMENTAL IMPACTS AND MITIGATION MEASURES ................... 36

F.1 Pre-Construction Phase ................................................................................................... 36

F.1.1 Design Project ........................................................................................................... 36

F.1.2 Pedestrian Crossings ................................................................................................ 36

F.1.3 Local Animal Passages ............................................................................................. 36

F.1.4 Removal of Roadside Vegetation .............................................................................. 36

F.1.5 Site Selection of Work Camps and Facilities ............................................................. 37

F.1.6 Local Water Resources ............................................................................................. 37

F.1.7 Selection of Borrow Pits............................................................................................. 38

F.1.8 Cultural, Historical and Archaeological Assets .......................................................... 38

F.1.9 Indigenous or Vulnerable People............................................................................... 38

F.2 Construction Phase .......................................................................................................... 38

F.2.1 Potential Impacts on Public Access, Utilities and Services ....................................... 38

F.2.2 Campsites.................................................................................................................. 39

F.2.3 Air Pollution ............................................................................................................... 41

F.2.4 Surface and Groundwater Resources ....................................................................... 42

F.2.5 Borrow Pit Operations and Excavations .................................................................... 42

F.2.6 Specific Construction Activities.................................................................................. 42

F.2.7 Potential Impacts related to Waste Management and Waste Disposal ..................... 43

F.2.8 Biodiversity and Ecological Resources...................................................................... 44

F.2.9 Decommissioning of Work Sites ................................................................................ 44

F.3 Operational Phase ............................................................................................................ 44

F.3.1 Air Pollution ............................................................................................................... 44

F.3.2 Noise Impacts ............................................................................................................ 45

F.3.3 Hazardous Material Spills .......................................................................................... 45

F.4 Cumulative impacts .......................................................................................................... 45

G. INFORMATION DISCLOSURE, CONSULTATION AND PARTICIPATION .......................... 47

G.1 Preparation Works ........................................................................................................... 47

G.2 Contacting Stakeholders and Public Announcement of the Venues................................ 48

G.3 Performance of the Public Venue .................................................................................... 48

G.4 Comments Received & Response ................................................................................... 48

G.5 Planned Information Disclosure ....................................................................................... 50

H. GRIEVANCE REDRESS MECHANISM................................................................................. 51

H.1 Grievance redresses levels .............................................................................................. 51

H.2 Grievance Coordinators and Focal Points, Complaints Recording and Reporting........... 52

H.3 Disclosure of the Grievance Process ............................................................................... 52

I. ENVIRONMENTAL MANAGEMENT PLAN............................................................................. 53

I.1 Institutional Strengthening ................................................................................................. 53

I.2 Cost Estimates for Mitigation and Monitoring Activities ..................................................... 54

J. CONCLUSIONS AND RECOMMENDATIONS....................................................................... 56

List of Figures

Figure -1 CAREC transport corridor ............................................................................................. 9

Figure -2 General project overview............................................................................................. 15

Figure -3 Detailed project overview ............................................................................................ 16

Figure -4 Potential sources of quarried construction material .................................................... 18

Figure -5 Photo of the Badam river within the city of Shymkent ................................................. 19

Figure -6 Protected areas and ecological values of Kazakhstan ................................................ 24

Figure -7 Working structure of NGO Sana Sezim....................................................................... 35

List of Tables

Table -1 Air quality standards ..................................................................................................... 12

Table -2 Soil quality standards ................................................................................................... 12

Table -3 The main technical features of the road ....................................................................... 17

Table -4 Cattle crossings locations ............................................................................................. 19

Table -5 Animal species registered in the South-Kazakhstan region ......................................... 23

Table -6 Bird species registered in the South-Kazakhstan region .............................................. 23

Table -7 Results of soil sampling along the Project Road compared with approved MAC in soils according to the local standards ................................................................................................. 26

Table -8 Air quality analysis along the Project Road compared with approved MACot  in air according to the local standards ................................................................................................. 28

Table -10 Wind regimes (Shymkent meteo station).................................................................... 29

Table -11 Production, investment and transport ......................................................................... 30

Table -12 Characteristic of population of the Project Area ......................................................... 32

Table -13 Employment in the Project Area ................................................................................. 33

Table -14 Indicators of living standards in South-Kazakhstan region ......................................... 34

Table -15  Summary of Costs for Environmental Safeguard Actions as Proposed in the EMP.. 55

Table -16  Cost Estimate for proposed Environmental Safeguard Training Activities ................ 55

List of Abbreviations

ADB	Asian Development Bank

Akim	Head of Administration (region, district & settlement) in Kazakhstan

Akimat	Administration of the region, district or settlement in Kazakhstan

AP	Affected Person

BTB	Bituminous treated base

CAREC	Central Asia Regional Economic Cooperation Program

CFH	MOA’s Committee of Forestry and Hunting

DESK	Department of Environment of South-Kazakhstan region

EEC	Environmental Expertise Committee EIA	Environmental Impact Assessment EMP	Environmental Management Plan

EBRD	European Bank for Reconstruction and Development

FS	Feasibility Study

GoK	Government of Kazakhstan

IEE	Initial Environmental Examination

IFI	International Financing Institution

IUCN	International Union for the Conservation of Nature

MOA	Ministry of Agriculture

MOEP	Ministry of Environmental Protection

MOH	Ministry of Health

MOTC	Ministry of Transport and Communication

NGO	Non-Governmental Organization

OVOS	Environmental Assessment conducted in accordance with Kazakhstan environmental legislation

PEIA	Preliminary Environmental Impact Assessment

PC	Public Consultation

RC	MOTC’s Roads Committee RoK	Republic of Kazakhstan RoW	Right of Way

SanPiN	Sanitary Regulations and Standards (Ministry of Health)

SES	Sanitary and Epidemiological Services of MOH

SNiP RK	Construction Standarts of the Republic of Kazakhstan

SPS	Safeguard Policy Statement, Asian Development Bank (2009)

SS EMP	Site-specific Environmental Management Plan

TSP	Total suspended particulate

List of Measurements

Ch km	Chainge kilometer

°C	Degree Celsius

dBA	Decibel (most common measure of sound)

ha	hectare

km	Kilometer

km2	Square kilometer

km/h	Km per hour

KZT	Kazakhstan Tenge (unit of currency)

m	Meter

m3	Cubic meter

Mac	Maximum allowable concentration

mg/m3	Milligram per cubic meter

m/s	Meters per second

EXECUTIVE SUMMARY

1 Introduction

This Initial Environmental Examination (IEE) has been prepared for the proposed rehabilitation of the Shymkent-Tashkent Road to ensure good environmental practice and documented compliance with the requirements of the Asian Development Bank (ADB). This road section is a

37 km segment located between km 705 and km 742 of the Shymkent – Tashkent road, which is going to be financed  by the ADB. The Project  has been classified  as Category  B. i.e., a project requiring an IEE pursuant to ADB Safeguard Policy Statement 2009.

The Project Proponent is the Government of RoK, acting through its Ministry of Transport and Communications  (MOTC) Roads Committee (RC) of the South Kazakhstan Oblast. The Project aims  to  contribute   to  regional  cooperation   and  trade  along  CAREC  Corridor  3  through rehabilitation of the road that connects Tashkent, the capital of Uzbekistan, and Shymkent, third largest city of Kazakhstan. The improvements  of the whole Shymkent - Tashkent road section are being financed by two international financing institutions (IFIs): ADB and EBRD (European Bank for Reconstruction and Development). The 37-km road section begins from the Shymkent city bypass’s end point, and passes through the territory of Shymkent and three districts of the South-Kazakhstan Oblast supported by ADB financing.

The projected traffic demands for Project Road Section at km 705 is about 32.000 vehicles per day in 2040 year that indicates  a clear need to upgrade  the highway  to technical  standards (SNiP RK 3.03-09-2006) for high speed roadways. Roads of this standard are considered to be warranted when calculated traffic in 20 years is estimated to be above 7,000 vehicles per day.

The objective of this IEE is to address the environmental impacts and management issues associated   with   the   proposed   road   rehabilitation.   The   IEE   report,   which   includes   an Environmental   Management   Plan   (EMP),   addresses   the  needs   of  applicable   laws  and regulations  of the Government  of Kazakhstan  including  the provisions  of the ADB Safeguard Policy Statement, June 2009.

The preparation of this IEE was undertaken through a desk study and field consultations with regional level representatives  of GoK and local stakeholders. The IEE Study is based primarily on earlier Project documentation including national environmental impact assessment, field investigations of an ADB’s consultant in April - June 2012, public consultation conducted in 24

May 2012 in Shymkent and informal consultations conducted in local villages: Rabat, Mambetov,

Aktas and Akzhar in June 2012.

2 Description of the Environment

The Project Area is located within the major geomorphic regions, such as piedmont plains and mountains of Western Tien-Shan (Kazygurt Mountains). The city of Shymkent and Rabat village, closest settlements to the Project Road are situated within seismic area with seismic intensity of seven and eight on the Richter scale. No records of catastrophic earthquakes were registered in the relatively recent past. The Project documentation indicates that potential sources of quarried construction materials are situated in the immediate area.

The Project Road does not cross any rivers. The closest surface water sources to the starting point of the Project Road are the Badam River and Badam water reservoir.

The Project Area located within South-Kazakhstan  region that can be characterized by sharply continental climate conditions. The number of foggy days is insignificant and more frequently happens  in  winter.  Thunderstorms   in  the  Project  Area  are  registered  year  round,  more frequently observed in summer.

The Project Area vegetation is represented by semi-savannahs multiyear and one-year grasses of the  ephemeral  type  and  ephemerals.  There  are  no  legally  protected  areas  or rare/endangered species habitats found within or in the close vicinity to the Project Road.

Economic  resources  in  the  immediate  vicinity  of  the  Project  Area  are  primarily  those  that support  dry  land  farming,  an  irrigation  network  and  the  grazing  potential  of  the  area's pasturelands.  No  minerals  are  known  to  be  exploited  in  the  immediate  Project  Area.  No industries or food processing facilities are known to exist in the Project Area.

There is very remote chance of finding any new sites of archaeological value in the Project Area as the alignment is completely within existing RoW with insignificant road widening.

3 Anticipated Environmental Impacts / Mitigation Measures and EMP

All potential positive and negative direct and indirect impacts on physical, biological, social and other valuable resources were considered in close consultation with the Design Engineers, developers of the national environmental assessment (OVOS) and in dialogue with a number of local stakeholders. As a result, it was found that there are no issues that cannot be addressed through standard mitigation measures.

Potential   risks   during   the   Pre-Construction   Phase   are   related   with   low   environmental management capacities of the Road Comittee of South Kazakhstan Oblast. During this phase, a major instrument to prevent possible environmental  and health impacts is the elaboration of a Site-Specific Environmental Management Plan (SS EMP). As this plan is required from each contractor, it is suggested to employ qualified experts who will assist the Contractors in fulfilling this task.

Much of the potential impacts relating to construction works are to be extensively addressed in each  SS  EMP.  Some  of  the  major  potential  impacts  during  this  project  phase,  and  the corresponding corrective measures, include: inclusion of public information and awareness campaigns at early work stage, provision for training courses, public awareness events and reporting of environmental damages; prevent hindrances and shortages for the general public utilities; specifications of permissive work hours for distinct construction activities; special consideration   of  precautionary  measures  while  operating  asphalt  mixing  plants,  crushers, bitumen and concrete works, stockpiling of materials; specification of handling, transporting and storing hazardous materials; management options to avoid potential impacts on surface/ groundwater resource, local biodiversity and ecological resources (particularly in the vicinity of Badam  forest  of local importance  and Kazygurt  mountains);  selecting  sites for work camps, following the established guidelines and close consultation with local communities.

Addressing traffic safety is probably the chief concern of all parties involved, when this road will be completed.  The  IEE  analyzes  the  main  causes  for  high  accident  rates,  and  accordingly proposes a number of actions to curb this. Maintaining good road conditions, provision of good signage  where  needed,  electronic  warning  tables,  emergency  phones,  traffic  controls  and proper enforcement, surveillance of the driving licensing process, fencing off wild and domestic animals  from  the  road,  and  regular  awareness  campaigns  are  considered  the  appropriate means of choice.

4 Conclusion and Recommendations

The  benefits  of  the  Shymkent  –  Tashkent  Road  Section  Project  justify  its  implementation, provided that the recommended mitigation actions are incorporated in its implementation. These benefits include a contribution to a more efficient transport network for use within the immediate Project  Area  and  for use  by regional,  national  and  international  traffic.Most  of the  potential impacts  are  temporary,  mostly  linked  with  the  construction  stage  and  can  be  mitigated  as proposed in the EMP.

A. INTRODUCTION

A.1 Project Background and Objective of the Study

1.      This  Initial  Environmental   Examination   (IEE)  has  been  prepared   for  the  proposed rehabilitation of the Shymkent-Tashkent Road to ensure good environmental practice and documented compliance with the requirements of the Asian Development Bank (ADB) reflected in the Safeguard Policy Statement. This road section is a 37 km segment located between km

705 (exact location according to the Design Documentation  is km 705+621) and km 742 (km

742+804)  of the Shymkent  – Tashkent  road, which is going to be financed by the ADB. The Project has been classified as Category B. i.e., a project requiring an IEE pursuant to ADB Safeguard Policy Statement.

2.              The Project Proponent is the RoK, acting through its Ministry of Transport and Communications (MOTC), Committee for Roads (CR). The Project aims to contribute to regional cooperation and trade along CAREC Corridor 3 through rehabilitation the road that connects Tashkent, the capital of Uzbekistan, and Shymkent, third largest city in Kazakhstan (Figure -1). The improvements  of the whole Shymkent - Tashkent road section are being financed by two international  financing  institutions  (IFIs): ADB and EBRD (European  Bank for Reconstruction and Development).  The 37-km section begins from the Shymkent  city bypass end point, and passes  through  the  city  of  Shymkent  and  three  districts  of  the  South-Kazakhstan   Region supported by ADB financing.

The objective of this IEE is to address the environmental impacts and management issues associated   with   the   proposed   road   rehabilitation.   The   IEE   Report,   which   includes   an Environmental   Management   Plan   (EMP),   addresses   the  needs   of  applicable   laws  and regulations  of the Government  of Kazakhstan  including  the provisions  of the ADB Safeguard Policy Statement, June 2009.

A.2 Methodology and Scope of the Study

3.               This  IEE  covers  the  applicable  national  and  ADB  environmental   requirements, description of baseline environmental conditions, environmental impacts associated with road rehabilitation, recommended mitigation measures and environmental monitoring program. The preparation of this IEE was undertaken through field consultations with regional level representatives of GoK and local stakeholders. The IEE is based primarily on earlier Project documentation  and field investigations  conducted  by a local consultant  in April - June 2012, public consultation conducted in 24 May 2012 in Shymkent and informal meetings conducted in local villages – Rabat, Mambetov, Akzhar and Aktas on 6 June 2012. The first detailed design on rehabilitation of Shymkent - Tashkent road, covering whole length and including considered part from km 705 - 742, was developed in 2004 by local Design Company KS-Engineering. First revision of the detailed design was done in 2007. The last version of the detailed design is being upgraded this year (2012) due to the recent changes in traffic volume.

4.               This IEE considers only ADB part of the whole Shymkent – Tashkent rehabilitated highway. Another Environmental Assesment will be developed for the remaining road segment financed by EBRD. ADB and EBRD have fairly comparable environmental safeguard processes. EBRD  as well  as ADB  use  same  environmental  categorization  system  with  IEE  supporting category B projects. All of this makes harmonization of two Environmental Assesments easier.

5. 	The  only  significant  difference  is  that  the  EBRD  does  not  require  consultation information   disclosure,  but  simply  recommends   it  and  usually  agrees  with  whatever  the proponent’s legal requirements is. Another issue is linked with difference in time and scheduele given for development  of two documents.  This IEE is planned to be submitted  by the end of June. The work on IEE report on the EBRD road section has been recently started and going to be finalized only in the middle of July 2012. Due to this fact it is proposed to implement a follow up harmonization approach in preparation of the IEE on the remaining EBRD section of the road. It means  that  some  relevant  parts  of  this  IEE  report  (ADB)  as EMP  and  outputs  of public

consultating can be used as a base for further aligment of the second IEE report developed by

EBRD consultant.

A.3 Study Area

6.               The geographic boundaries are taken as 200 m on either side of the road due to the absence   of  any  special   environmental   condition   and  presence   of  dominating   terrestrial environment. There is no specific airshed or aquatic and acoustic environment, as well as no nationally significant or protected site, situated along the Project Road.

7.               The starting point for the Project is located on the existing highway named A2, at the border of Shymkent city bypass end point, and passes through territory of the city of Shymkent and three administrative districts of the South-Kazakhstan Oblast: Tole bi, Sairam and Kazygurt.

8.               The Project Road is a section of the shortest way from Shymkent to the Uzbekistan where rehabilitation  in linked with modernisation  of the existing 37-kilometer  existing four-lane road meeting all applicable RoK technical standards.

9.               The Project will require the dedication  of 37 kilometres  of right-of-way  (ROW) and the areas for ancillary features such as bus stops and rest areas, and will require only land for temporary use for construction camps and related facilities. Its estimated cost is approximately US$ 125 million.

10.             On the average, the potential direct area of influence along the entire length of the Project  Road  is  an  estimated  about  27.5  m  width  strip  within  the  ROW.  According  to  the construction norms of Kazakhstan (SNiP RK 3.03-09-2006) the width of right-of-way for road of the 1st technical category (different from environmental classification of ADB) may vary from 30 m to 70 m depending of inclination. However according to the information provided by Designer Company “KS Engineering” the width of right-of-way in the Project Road section is 62 m. This area is expected to be directly affected by reconstruction of road embankment and embankment slopes. The extended area of influence will include borrow areas and access roads, contraction camps, working and construction materials storage sites and watercourses in the vicinity.

Figure -1 CAREC transport corridor

Source: Drawn by ADB National Environmental Consultant based on materials of Central Asia Regional

Economic Cooperation Program-  www.carecprogram.org

B. POLICY, LEGAL, AND ADMINISTRATIVE FRAMEWORK

11.             The Project is required to comply with the environmental  requirements  of the RoK

and the requirements of the financing organization, in this case the requirements of the ADB.

B.1 Kazakhstan Government Environmental Laws, Regulations and Guidelines

B.1.1 Environmental Impact Assessment and Ecological Expertise

12.             Environmental protection is administered by the Ministry of Environmental Protection (MEP)  in Kazakhstan.  The Environmental  Code was adopted  in January  9, 2007 and is the basic legislative  framework  for environmental  protection  activity. The last edition available  on the MEP web-site is dated to January 30, 2012. According to Article 36 of the Environmental Code development of OVOS (EIA) is obligatory for all types of activities that can have a direct or indirect  impact  on  the  environment  or  health  of  the  people.  The  permitting  system  is  a component of the Environmental Code.

13.             The procedures  ensure  that projects  are environmentally  sound  operate  on three levels: Environmental Expertise Committee (EEC); Department of Environment of South- Kazakhstan region (DESK); Project Proponent (MOTC).

14.             The EEC is located in the capital and has the first and last word on all national level EIAs.  After  the  approval  of  a  terms  of  reference  (ToR)  and  the  selection  of  a  licensed Environmental Assessment (EA) specialist consultant, a preliminary environmental assessment (PEIA)  (essentially  a  scoping-level  desk  study)  is  prepared  in  parallel  with  an  engineering feasibility study.

15.             The DESK reviews the PEIA and provides written comments to the EEC. If needed, specialists  from within the Regional Department  of Agriculture’s  Water Resources  Committee and  Forestry   and  Hunting   Committee   and  from   the  Ministry   of  Health’s   Sanitary   and Epidemiological Services (SES) are asked to contribute. The available documentation indicates that in practice this is rarely done. In principal, the EEC receives the comments and recommendations,  reviews/edits  them, and the preparation  of an EIA is authorized.  Following review and approval of the EIA, it is sent to the Executing Agency (EA) for action.

16.             The Proponent Agency, in this case MOTC, is the third level. As the Proponent for the proposed action, it is responsible for required environmental actions and enforcement of the stipulations   of  the  EIA  prior  to  and  during  the  Project's  detailed  design  stage  and  for coordination of recommended environmental actions thereafter.

17.             The  consultant  who  prepares  the  PEIA  (PredOVOS)  usually  undertakes  the  EIA (OVOS)  and  proceeds  with  the  detailed  analysis  focusing  on  field  work  and  primary  date collection, with strict reference to Kazakhstan norms and codes. The focus of the EIA is the preparation  of a comprehensive  environmental  mitigation  and monitoring  plan (EMP),  in the past prepared  separately  and referred  to as an Ecological  Passport,  but now included  as a section of the EIA. Usually the EIA is prepared on the base of already available decisions undertaken by engineers and included in Detailed Design Study.

18.             The EIA undergoes a similar review; first at the regional level and then by Ministry of Environmental   Protection   (MOEP)   and   any   other   agencies   MOEP   decides   to  include. Comments are reviewed, edited and assembled by the MOEP. This step takes up to 30 days, after which the EIA authors are required to defend the EIA at a consultation session with all stakeholders in attendance. During this period the public can comment on the EIA, but receive only one announcement  in a local newspaper that the EIA is available for review. After EIA is complete, there is a public debate where the authors and the Proponent can answer questions from anyone. Once complete, the EIA is revised; a final document is prepared; and a certificate to proceed to the next stage is given to the proponent.

B.1.2 Other Environmental Legislation Relevant to the Project

19.             The  Water  Code  passed  in July 2003  contains  main  directives  on environmental protection,  preservation  and use of water resources  on the territory  of Kazakhstan.  The last changes were integrated in February 12, 2009.

20.             The main state document regulating land use and protection is the Land Code of the

Republic of Kazakhstan that was adopted in June 20, 2003.

21.             The Forest Code adopted in 2003 regulates the use, protection and conservation of forests as well as forest restoration. Specific issues related to the protection and conservation of forests, are regulated in by-laws: for instance, the 2002 governmental resolution on Measures of Haloxylon ammodendron tree conservation, the 2002 government resolution on Rules for compensation of damage to forestry and the 2001 government resolution on damage caused by illegal collection, logging, damage or destruction of plants in the Red Book, and the decision on Rules of forest safety. In 2004, the Parliament adopted a new version of the Forest Code.

22.             The Law of the Republic of Kazakhstan  ‘On the road’ dated 17 July 2001 laid the basic legal, economic and organizational principles of governance roads in the Republic of Kazakhstan and set their order. Article 2, Paragraph 2 of the Law «On the road» states that if international treaties ratified by the Republic of Kazakhstan launch other rules than those established by this Act the rules of the international treaties shall apply.

23.             For  the  construction  and  maintenance  of  roads  of  common  use,  land  users  are provided with the land for a ROW on the basis of established norms, depending on the roads category  and  under  the  project  documents.  The  size  of  the  ROW  for  projected  roads  for common use is set depending on the category under the rules of allotment of land for roads of public use, namely: for roads of I technical categories - 35 meters from the roads axis, for roads of II technical categories - 20 meters, for roads of III technical categories - 15 meters, for roads of IV technical categories - 13 meters, for roads of V technical categories - 12 meters. Road’s ROW  lands  are in the  possession  and  use  of road  authorities  or concessionaires,  and  are intended only for the development, improvement of roads and the establishment of road service. In the ROW of roads of common use is forbidden to carry out any kind of works or to place any buildings without the permission of the appropriate authorities.

24.             The  development   of  project   documentation   for  the  construction   of  new  and rehabilitation  of existing roads carried out in accordance  with the Law «On the road» and the legal and technical documentation used in the design and construction of roads. The main construction  standards  are  SNiP  RK  3.03-09-06  “Roads”  and  CN  RK  3.03-19-2006.  Both represent standard technical documentation based on “Regulatory legal acts and engineering regulations  in  sphere  of  architecture,  town  planning  and  construction,  effectual  within  the territory of the Republic of Kazakhstan”.

25.             The developed project documentation  is adjusted and checked for compliance with all rules and requirements in the construction and design of roads with executive bodies in the roads and state construction committee.

B.1.3 Air and Soil Quality

26.             Environmental Code defines the basic terms and principles of State control of air and soil conditions. In addition to the environmental legislation developed by MEP, Ministry of Health (MOH)  of  RoK  establishes  additional  Sanitary  Regulations  and  Standards  (referred  to  as "SanPiN") aiming protection of human health.

27.             Ambient air and soil quality standards are established by the last published SanPiN called  “Sanitary  and  Epidemiological  Requirements  for  Atmospheric  Air  in Urban  and  Rural Areas,   Soils  and  Their  Protection,   Maintenance   of  the  Territories   of  Urban  and  Rural Settlements,  Working  Conditions  with  Sources  of  Physical  Impacts  Affecting  People"  was introduced by the Decision Government of RoK, dated January 25, 2012.

28.             This document contains the information on the MAC of the harmful substances in the air and soil provided in table -1 and table -2.

Table -1 Air quality standards

| Substance | Maximum Allowable Concentration, mg/m3 | Hazard Class |
| --- | --- | --- |
|  | One Time Maximum | Daily Average |  |
| Inorganic dust | 0.3 | 0.1 | 3 |
| Nitrogen Dioxide | 0.2 | 0.04 | 2 |
| Sulphur Dioxide | - | 0.125 | 3 |
| Carbon Monoxide | 5.0 | 3 | 4 |

Source: “Sanitary and Epidemiological Requirements for Atmospheric Air in Urban and Rural Areas, Soils and Their Protection, Maintenance of the Territories of Urban and Rural Settlements, Working Conditions with Sources of Physical Impacts Affecting People", dated January 25, 2012

Table -2 Soil quality standards

| Substance | Maximum Allowable Concentration, mg/kg | Limiting Rate |  |
| --- | --- | --- | --- |
| Manganese (gross form)* | 1500 | According to the General Sanitary Norms |  |
| Cupric (flexible form)* | 3.0 | According to the General Sanitary Norms |  |
| Lead (gross form) | 32.0 | Translocational |  |
| Zink (gross form)* | 23.0 | Translocational |  |
| Arsenic (gross form) | 2.0 | According to the General Sanitary Norms |  |

Source: “Sanitary and Epidemiological Requirements for Atmospheric Air in Urban and Rural Areas, Soils and Their Protection, Maintenance of the Territories of Urban and Rural Settlements, Working Conditions with Sources of Physical Impacts Affecting People", dated January 25, 2012

* due to the absence of these substances in new SanPiN data was taken from the previous document «Standards of the Maximum Allowable Concentrations of the Hazardous Substances, Harmful Microorganisms and Other Biological Materials

Being the Soil Pollutants» approved by the Order of the Ministry of Health of the

RoK №99 dd 30.01.2004 and Order of the Ministry for Environmental Protection of the RoK №21П dd 27.01.2004.

B.1.4 Noise

29. 	The sanitary rule regulating on noise level within settling areas is SanPiN of RoK №

3.01.035-97  «Maximum  Allowable  Noise  Levels  in  Residential  and  Public  Buildings  and  in

Residential Areas».

30. 	The level of the road traffic noise is determined according to the norms of the SNiP (construction   norms  and  rules)  II-12-77  «Noise  Protection».  The  limit  of  noise  exposure

noise sources in compliance with the SNiP II-12-77 is 70 dBA.

31.             In addition to establishing acceptable standards, noise levels are generally regulated with  respect  to sound  levels  at specific  places  referred  to as "sensitive  receptors"  such  as schools,  hospitals  or,  in  the  absence  of  such  facilities,  at  residential  buildings  or  a  given distance from the source of the noise. No sensitive receptors potentially affected by either construction noise or operational noise were indicated or are known to exist in the Project Area.

B.2 Asian Development Bank (ADB) Environmental Policies and Guidelines

32.             The Project has been classified as a Category B project under the provisions of the ADB’s Safeguard Policy Statement (July 2009). ADB uses a classification system to reflect the significance of a project’s potential environmental impacts. A project’s category is determined by the  category   of  its  most  environmentally   sensitive   component,   including   direct,  indirect, cumulative, and induced impacts in the project’s area of influence. This project is classified as category  B due to the fact that its potential  adverse  environmental  impacts are less adverse than those of category A projects. These impacts are site-specific, few if any of them are irreversible,  and in most  cases  mitigation  measures  can  be designed  more  readily  than  for category A projects.

33.             The  scope  of  IEE,  according  to  the  ADB  requirements,  examines  the  project’s potential negative and positive environmental impacts and recommends any measures needed to prevent, minimize, mitigate or compensate for adverse impacts and improve environmental performance.   An   Environmental    Management   Plan   detailing   the   mitigation   measures, monitoring  program,  institutional  strengthening  and  implementation,  schedule  and  costs  are also included in this IEE.

34.             The IEE report will be presented to both the Government  of Kazakhstan  and ADB and shall serve as a background document for approval by the competent authority MOEP. The Project Proponent (MOTC) will have to make the draft IEE Report available in Kazakhstan at a public place accessible  to project-affected  groups and local NGOs. Once the IEE report has been locally disclosed and officially received by the ADB, the Bank will also make it available to the public before it begins formal appraisal of the project.

35.             It is important to note that, to be meaningful, the recommendations of an IEE and the EMP must go beyond recommendations  and become legally enforceable  and incorporated  in the bid and contract documents.

B.3 Administrative Framework

Project Area.  The Project Road passes through four sub-administrative  territorial units of South- Kazakhstan region, in particular:

    Section km 705 – km 713 (8 km) passes through Shymkent city;

    Section km 713 – km 728 (15 km) passes through Sairam district;

    Section km 728 – km 737 (9 km) passes through Tole bi district;

    Section km 737 – km 745 (8 km) passes through Kazygurt district.

36.            The management and monitoring of environmental aspects of the proposed road rehabilitation project shall involve the following government agencies:

(i)  Road Committee under the MOTC is responsible for planning, constructing, operating and maintaining of national roads in Kazakhstan. The Project Implementation Unit (PIU) of the local sub-division of the Road Committee (RC) in South-Kazakhstan  region will be in charge  of  project  management   to  ensure  that  appropriate  mitigation  measures  and monitoring programme and that the contract provisions are properly implemented. The RC of South-Kazakhstan region, as local level representative of the Project Proponent, responsible for coordination the IEE study, carry out required public consultations, ensure

implementation  of the EMP and public  disclosure  of the IEE study.  The RC shall also lease with relevant government offices for securing environmental approvals. During the operational phase of the Project, RC will undertake routine monitoring on road safety, the storm water drainage system, the condition of plantations, etc.

(ii)  The district offices of RC in Sairam, Tole bi and Kazygurt districts will undertake day- today supervision of construction and oversight of the implementation of environmental management plans during project implementation.

(iii) Department   of  Environment   of  South-Kazakhstan   region   (DESK)   shall  be  also responsible  for routine  monitoring  of the project  to determine  compliance  with environmental regulations and standards.

(iv) Sanitary and Epidemiological Services (SAS) of MOH in South-Kazakhstan  region will undertake  routine  monitoring  of  the  living  conditions  and  sanitary  provisions  at  the contractor’s work camp and worksites. MOH’s SAS shall be also involved in approving the contractor’s work camp installations and facilities and their compliance with the relevant sanitary and health norms and guidelines.

C. DESCRIPTION OF THE PROJECT

C.1 Main Technical Features

37.             The  main  objective  of the Project  is to reduce  road  transport  costs  and  improve access, transit and safety within Kazakhstan's North-South corridor, through the rehabilitation of the Project Road. For road users, the Project would lead to better road quality meeting mid-term traffic projections, better safety standards, lower travel costs and a shorter travel time.

38.             The Project is aims at upgrading Shymkent – Tashkent Road Section existing four- lane highway, dual carriageway with a centre median for its entire length. Its start point at km

705 (exact location according to the Design Documentation  is km 705+621) is the end of the

Shymkent city bypass. Its end point at km 742 (exact location according to the Design Documentation  is km  742+804)  connects  with  the  EBRD  Road  Section  (km  742-804).  The Project and its environs are illustrated by Figure - 2, 3.

39.             The Project includes road surface rehabilitation  works with saving of existing road alignment.  The  existing  grade  separated  interchange  will be replaced  by a new  one  at km

732+963. The Project also includes rehabilitation  of animal and agricultural machines passes,

replacement of existing culverts and electricity lines.

40.             The  Kazygurt  mountain  pass  road  has  a  quite  large  gradient.  As  reported  by Desinger  Company’s  Chief Engineer,  it is considered  to change elevation  of the road in this section of the rehabilitated road in order to decrease the existing maximal slope to at least 6%. However his words weren’t supported by any adequate longitudinal profile of the road.

Figure -2 General project overview

Source: Drawn by ADB National Environmental Consultant based on field trip survey

41.             Appendix  1  provides  the  typical  cross-sectional  characteristics  of  the  proposed upgraded  roadway.  In  total  seven  cross-sections  are  designed,  but  they  differ  only  in  that portions meeting technical standards including a barrier incorporated in the design of the centre median. These profiles and the Project's other design and construction standards will conform to the standards of Kazakhstan Technical Category I-B (Kazakhstan SNiP RK 3.03-09-2006). All of the proposed works will be accommodated  within the existing Right of Way (ROW), which varies from 30m to 70m. The main technical features are shown below in Table -3.

42.             The Project will include the construction of installation or rehabilitation of 36 culverts. Conditions  of most of the roadway's existing culverts were found to be poor. The Project will replace all culverts.

Figure -3 Detailed project overview

Interchange at km 732+!963

end point (km 742+361

43.             A total of 1,621 trees  located mostly within central separation  lane are slated for removal for this road segment.   According   to   the   state   forests'   accountancy   all   trees situated  along road serving as protection greenery within ROW are under responsibility of RC.

However  all trees of South-Kazakhstan  are under the management  of the South-Kazakhstan region  Territorial  Office  of  the  Committee  of  Forestry  and  Hunting  (CFH).  A  program  for essential tree cutting to implement the Project is planned to be developed with and approved by the South-Kazakhstan regional CFH close to the beginning of the construction works. All expenditures   on   removal   of   old   and   plantation   of   new   trees,   together   with   financial compensations going directly to the state budget, are included in the construction costs. In total

6,488 trees will be planted according to the information provived in the OVOS report.

Table -3 The main technical features of the road

| Name of the road component | Size | Comment |
| --- | --- | --- |
| Total length of the Project Road | 37 km |  |
| Number of lanes | 4 |  |
| Highway width | 27.5 m | total |
|  | 15 m | one-way |
| Central median | 5 m |  |
| Maximum shoulder width | 3.75 m |  |
| Cross-fall in the carriageway | 3% |  |
| Design speeds | 150 km/h | for flat |
|  | 100 km/h | for undulated terrain |
|  | 60 km/h | for hilly terrain |
| Road surface |  | concrete cement |
| Grade separated interchange | 1 | rehabilitation of existing one |
| Animal/agricultural machines crossings | 3 | rehabilitation of existing ones |
| Water culverts | 36 | replacement of existing ones |
| Electricity lines | 9 | replacement of existing ones |
| Bus stops | 6 |  |
| Amount of excavation | 620.000 m3 | mainly close to the Kazygurt bypass |
| Amount of fill | 230.000 m3 |  |

Source: Developed by ADB Environmental Consultant based on Design documentation

44. 	There are some potential sources of quarried construction material identified by the available Project documentation. Most of them are existing operations located out of the Project Road  (Figure  -  4).  Transportation  of  the  construction  materials  from  four  of  the  proposed sources will require passing through populated areas (the city of Shymkent).

45.             Although the Project Road will be primarily concrete cement, it will use asphalt for various  purposes  including  rehabilitation  of  adjacent  local  roads  and  the  sub-base  for  the roadway. The available Project documentation  proposes only one location for asphalt concrete plant within construction camp at km 724 (Figure - 4).

46.             The Project Road section from km 705 to km 742 includes one construction camps are proposed  to locate at km 724. The total area of a proposed  construction  camp is about

22.000 m2.

Figure -4 Potential sources of quarried construction material

Source: Detailed Design documentations provided by local Designer Company KS-Engineering LLC

47.             No  specific  location  of  storage  areas  is  provided  in  the  Design  documentation. However  as reported  by Main Design Engineer  of KS Engineering  all of them will be placed within ROW.

48. 	The Project documentation indicates that water for construction might be taken from the Badam River passes through the city of Shymkent. No exact locations of water extraction from the rivers are identified. Nevertheless, possible sourcing places can be discovered close to the road are located within the Shymkent city in the vicinity of the settling area (Figure -5).

49.             The drinking water for construction camps is planned to be drawn from the existing water  supply  system,  possibly  the  city  of  Shymkent.  No  preliminary  agreements  with  local authorities of the city are available in Design documentation and local EIA (OVOS).

50.             There is no need of importing filling materials. If the amount of excavation ground is about 620.000 m3, the amount of required filling ground is just about 230.000 m3.  All ground will be excavated while construction of the lower road near Kazygurt mountains that will be reused as fill material.

51.             There are four existing cattle passages three of them are combined with agricultural machinery passes that represent well built concrete structures. All existing cattle (agricultural vehicles) crossings (Figure -3 and Table -4) are planned to be replaced with preservation  of their current geometric shape and technical features. The cross-section of rehabilitated cattle passage integrated with agricultural machinery passage is provided in Appendix 1.

52.             There is an existing grade separated interchange that is going to be demolished and to be replaced by a new one at km 732+963.

53.             The  Project  considers  rehabilitation  of  four  existing  rest  areas,  which  includes replacement  and re-planning  of the existing surface. The project includes installation  of 6 bus stops  supplied  with  shelters.  The  width  of the  bus  stop  sites is 3.75  m, and  length  is 13m. Stopping areas of the bus stops are separated from the roadway by a dividing strip of 0.75 m in width. According to the Designer Company KS Engineering all bus stops and rest areas are equipped with toilets.

Figure -5 Photo of the Badam river within the city of Shymkent

Source: Photo taken by ADB Environmental Consultant during the field survey

Table -4 Cattle crossings locations

| Project km | Size | Comment |
| --- | --- | --- |
| 725+600 Animal/agricultural vehicles crossing | Rectangular tube 6m*4.5m | Replacement |
| 729+400 Animal/agricultural vehicles crossing | Rectangular tube 6m*4.5m | Replacement |
| 735+700 Animal crossing | Rectangular tube 4m*2.5m | Replacement |
| 741+100 Animal/agricultural vehicles crossing | Rectangular tube 6m*4.5m | Replacement |

Source: Developed by ADB National Environmental Consultant based on Design documentation

C.2 Traffic Forecast

54.             Project Road section is a part of the CAREC 3 transit corridor linking Western and Northern countries  of Eurasian  continent with South and Central Asia through the territory  of Kazakhstan. The projected traffic demands for Project Road Section at km 705 forecasted by Designer Engineers is about 23.000 vehicles per day in 2040 year. Roads of this standard are considered to be warranted when calculated traffic in 20 years is estimated to be above 7,000 vehicles per day.

D. ANALYSIS OF ALTERNATIVES

55.             The  designs  under  consideration  by the  DEs  were  based  on  the  findings  of the previous feasibility study, which considered the option without project and the upgrade highway option. Then the design engineers developed the Project components  based on the feasibility study, and they were not therefore required to consider alternative alignments.

56.             Given  the  infrastructure  setting  and  enormous  distances  covered  by the  CAREC transport corridor, as well as traffic patterns and limited connectivity, a feasibility study prepared by the RoK rejected the other transport modes as they appeared uneconomic. Road corridor development was given preference over the expansion and rehabilitation of the railway network because roads are judged to be more cost efficient; faster to construct; serve local demands more  flexibly;  and  are  ultimately  less  complicated.  Rail  gage  standards  are  not  compatible among East Asian, Central Asian, Iranian and Central European systems, thus incurring much handling  and processing  of cargo.  The railway  alternative  was also rejected  due to the low quality of actual services and elevated risks for food cargo.

D.1 "No-Project" Option

57.             Without the Project, the road would continue to be somewhat of a logistic obstacle to road transport form along the CAREC 3 corridor and the economic benefits to Kazakhstan and surrounding  economies  (Uzbekistan)  would not be realized.  Many sections  of the road have some parts where the wearing course is damaged. This condition adversely affects traffic safety and  reduces  vehicle  speeds,  as  well  as being  an impediment  to safe  overtaking  of slower vehicles.  In general, the environmental  conditions  along the road would continue  as present. The measures foreseen for environmental  mitigation and increased traffic safety as per design of the project, such as improved run-off management and control, noise screens, dust control, safer cattle and agricultural  machines passes and speed control measures would not, or to a much lesser extent be realized.

58. 	The option of "No-Project" has been considered and found to be neither reasonable nor prudent in light of the Transport Policy Framework and the Transport Strategy developed by the Republic of Kazakhstan to improve and expand the network over the short to medium term.

59.             Improvement  of Shymkent - Tashkent Road Section is an important element within this overall Transport Strategy which has identified the goal of making the road system larger, better,  more  accessible,  more  affordable,  more  efficient,  safer,  and  more  environmentally friendly.  The  Transport  Strategy  established  a program  which  identifies  priority  investments such as the improvements  to Shymkent  - Tashkent  Road Section and failure to improve  the road section  could  seriously  undermine  the financial  underpinnings  of this program.  As also noted in the introductory section, Shymkent - Tashkent Road Section is an important element of the transport corridor CAREC 3, facilitating traffic and international trade between Russian Federation and South Asia and Middle East countries.

60.             The   “No-Project”   case   might   cause   transportation   delays,   increase   of   road congestions and accidents, road side environmental pollution and other negative impacts linked with lack of the existing road technical capacities to carry out growing traffic pressure. At the end all of these might lead to the extra expenses and increase of the road transportation costs though the territory of Kazakhstan.

D.2 Design Alternatives

61.             The terminal  points of the Road Section  km 705-742  are established  by the road network to which the Road Section will connect. Main technical need to upgrade the roadway to technical standards (SNiP RK 3.03-09-2006) for highways. Major components of the design, particularly the accommodation  of animal and farm equipment crossings at strategic points are sound mitigation actions to lessen public and animal safety issues.

62.            Cement-concrete with bituminous treated base (Btb) meeting Kazakhstan technical standards  was selected  as the road surface  in accordance  with the technical  design  project

which  identified the  need  for  rigid pavement  with enhanced  heavy-duty  road  surfacing.  The selection  was  made  based  on:  (i)  lower  construction  and  transport  costs;  and  (ii)  better adaptability   to  the  sometimes   harsh   local  winter   conditions,   thus   reducing   repair  and maintenance costs.

E. DESCRIPTION OF THE ENVIRONMENT (BASELINE DATA)

E.1 Ecological Environment

E.1.1 Fauna

63.             Overview.  Most of the indigenous mammals found in the Kazakh Steppe burrow, live in  colonies,  or  migrate.  Those  typically  found  include  numerous  rodents  such  as  ground squirrels  (Citellus),  hamsters  (Cricetus,  Cricetulus,  Podopus),  voles  (Microtus),  birch  mice (Sicista), lemmings (Lagurus), marmots (Marmota bobac); and lagomorphs such as pikas (Ochotona)  and  hares  (Lepus).  Wolf  (Canis  lupus),  foxes  (Vulpes  vulpes,  V.  corsac)  and Siberian polecat (Mustela eversmanni) are typical steppe carnivores. More detailed information on popular animals and birds types in the region is provided in Table -5 and Table -6.

Table -5 Animal species registered in the South-Kazakhstan region

| Years | Main types of the animals |
| --- | --- |
|  | Siberian Roe Deer | Siberian mountain goat | Wild boar | Jackal | Fox | Corsac | Wolf | Tolai hare | Muskrat | Badger |
|  | In numbers |
| 2005 | 269 | 1949 | 1038 | 655 | 5300 | 298 | 471 | 11000 | 8338 | 2417 |
| 2010 | 305 | 2034 | 1419 | 808 | 5763 | 362 | 955 | 9624 | 10136 | 2370 |

Source: Data provided by CFH of South-Kazakhstan region

Table -6 Bird species registered in the South-Kazakhstan region

| Years | Main types of the birds |
| --- | --- |
|  | Pheasant | Gooses | Ducks | Coot | Pigeon | Quail | Chukar | Partridge |
|  | In numbers |
| 2005 | 14470 | 50125 | 175354 | 218250 | 27500 | 214750 | 20400 | 50250 |
| 2010 | 29215 | 62894 | 209170 | 162783 | 46156 | 217219 | 24271 | 50134 |

Source: Data provided by CFH of South-Kazakhstan region

64.             Project Area. There are no endangered species habitats found within or in the close vicinity  to  the  Project  Road.  The  most  popular  animals  inhabiting  the  Project  Area  are rodents: squirrels, jerboas and field mice. Among the insectivores there are hedgehogs, shrews, also reptiles like lizards and snakes. However there are very few in numbers mostly due to the intensive agricultural developments situated along the existing road for a long time. The most common livestock species are cattle and sheep.

65.             The only few types among  rare species  of insects   like Satanas  gigas and Sphex flavipennis listed in the "Red Book" of Kazakhstan are registered in the Project Area. No places of permanent nesting and wild animals’ habitats were discovered adjacent to the road.

66.             The Badam River and small Akzhar Lake are locally popular fishing places situated close to the Project Road. As reported by South-Kazakhstan  region CFH the rivers and Akzhar lake  contains  long-horned  beetles,  a  large marinkas, carp, catfish  and  other  river  species. However, these resources are not significant enough to have commercial  value and are used mostly for amateur fishery.

E.1.2 Flora (Vegetation and Plant Species)

67.             Project Area.  The Project Area vegetation represented by semi-savannahs multiyear and  one-year  grasses  of  the  ephemeral  type  (Poa  Bulbosa,  Carex  etc.)  and  ephemerals (Bromus   tectorum,    Bromus   Japanese,    Aegilops   etc.).   There   is   significant    presence of bluegrass, mustard  and stickseed. Among  rarely distributed species are ferula  types.  There are also meadow species like wheat grass, yarrow, licorice, etc. The average density of grass stand is just about 50-60%. The average height of the grass stand is 20-25 cm.

68.             Most of the lands along the road are used for crop production and livestock breeding. Among  cultivated  plants  there are wheat,  alfalfa, safflower, corn, cotton,  melons  and gourds.

The     most     frequently     appearing     weeds     in     the     area     are     Picris,     Sorghum halepense, Convolvulus, Cynodon, Phragmites.

69.             There are no natural forest lands along the entire ROW. As the Project Road passes within the old alignment no serious impacts on vegetation and plant species growing near the existing road are expected. The forest plantations located almost along the existing road are generally at a distance of 10-40 meters (more than 50 meter near Badam leskhoz at the starting point  of  the  road  alignment).  There  are  also  some  trees  located  in  the  central  green  road separation area and along two sides of the road within the ROW. These trees fall under the management  of the South-Kazakhstan  regional  territorial  office of the Committee  of Forestry and Hunting (CFH). The most popular and adopted to local climatic conditions among existing types of threes is elm.

E.1.3 Sensitive Habitats & Protected Areas

70.             Overview.  IUCN indicates that the Project Area is within the area delineated as the

"Mountains  of  Middle  Asia  Centre  of  Plant  Diversity"  and  one  of  the  WWF  Global  200

Ecoregions  as  illustrated  by  Figure  -6.  The  designation  offers  no  legal  protection,  but  is indicative of the relative importance of the area.

71.             Project  Area.  There  are  no  legally  protected  areas  or  rare/endangered  species habitats found within or in the close vicinity to the Project Road. As reported by the head of the South-Kazakhstan  region CFH the closest protected area is reported to be more than 50 km distant.

72.             However there is forest of local importance serving as a city protecting shelter called Badam leskhoz. There are some fruit trees like apple, apricot and pear trees are growing on the territory of Badam leskhoz. No trees belonging to the Badam leskhoz are going to be cut or impacted due to the large distance from the road (more than 50 m), as reported by Designer Company KS Engineering and approved by CFH of South-Kazakhstan region.

Figure -6 Protected areas and ecological values of Kazakhstan

Source: UNEP – Program of Preservation of Natural Habitat in Kazakhstan

E.2 Physical Environment

E.2.1 Geologic Characteristics & Resources

Overview.  The  South-Kazakhstan   region  is  located within  major  geomorphic  regions, such as piedmont plains and   mountains    of   Western    Tien-Shan.    Project   Area.   The   Sairam district territory is located  within the piedmont plains and the surface  slopes from southeast to northwest.   The   main   elements of   the   relief are undulating low   hills and   depressions. The hills have a rounded shape and their slopes facing in different directions with the height ranges from 10-20 meters    and    more.    The    steepness    of the    slopes    is different    and    varies from flat to gently rolling. The Kazygurt district represents smaller part of the Project Area with low mountains and ridges, like Kazygurt Mountains that appear right after the end point of the Project Road.

73.            Given these geological conditions and as evidenced by history, the Project Area is seismically  active.  Earthquakes  with magnitudes  of six-eight  points  on the Richter  scale are possible    there    according    to   the   local    normative    document    SNiP    RK 2.03-30-2006 "Construction in seismic regions". The city of Shymkent and Rabat village, closest settlements to the Project Road are situated within seismic area with seismic intensity of seven and eight on the Richter scale. However there were no records of catastrophic earthquakes registered in the relatively recent past.

74.             Overview.  The South-Kazakhstan  region is reach in mineral resources.  There are deposits of polymetallic ores, which are located on the western slope of the Karatau ridge. The construction  materials like limestone  and dolomite for lime and cement, silica sand, refractory, ceramic   and   bentonite clays, mineral   paints,   sand   and gravel   are   available   within   the region. There  are  also deposits   of phosphates,   marble,   stone  cladding,   fluxing  materials, jewellery  and ornamental   stone,  lead  and gold.  Project  Area.  The  Project  documentation indicates that potential sources of quarried construction  materials in the immediate area have been identified as follows:

	ShDS is  existing quarry for natural gravel and sand mixture located at km 665 6 km on the right (north) about 46 km away from the start point (km 705) of the Project Road with the access via existing the Shymkent city bypassing road;

	Ashy Bulak is existing quarry for natural gravel and sand mixture located at km 665 4 km on the left (south) about 44 km away from the start point (km 705) of the Project Road with the access via existing the Shymkent city bypassing road;

	Arys sand quarry located at km 698 70 km on the left (south) on the west from the start point  (km  705)  of  the  Project  Road  with  the  access  via  existing  the  Shymkent  city bypassing road.

75. 	Project Area.  The northern part of the Shymkent city is crossed by the Badam river valley. Maximum altitude   of   the   Project   Area   within   Sairam   district is   939 meters. The minimum altitude is 382 m at the edge of the watercourse Shubursu on southwest of the district. The  northern  part  of the  Kazygurt   district is  formed  by  watershed ridges of  Kazygurt and Karzhantau. Maximum altitude within the Kazygurt district is 3615 m. The topographic, climatic and soil conditions (discussed below) are such that most of the lands along the Road Section km 705-742 ROW are used for agricultural, including use as pastures and crop production.

E.2.2 Soil Characteristics

76.             Dominant soils existing within the Project Area are:

The submontane  brown soils are met as the separate solid masses on the high submontane plains.  They  are  formed  under  the  coarse-grained  ephemerides  (bulbous  barley,  Agropyron villosus) with marked additions of the common mesophilous  cereals (cocksfoot) and savanna- like tall grasses.

The submontane gray-brown soils are frequently met in the upper belt of the submontane plains. They  were  formed  under  the  coarse-grained   ephemerides  vegetation  (Agropyron  villosus, bulbous barley) and savanna-like tall grasses. The soil materials are represented by the heavy loess  loams  mostly.  The  gray-brown  soils  have  the middle  or deep  thickness  of the humid horizons.

The submontane common gray soils and light, northern serozems are widely spread on the submontane, partly foothill plains. The common gray soils occupy the upper, well watered belt of the gray soil zone; the light serozems occupy the lower belt. On the submontane plains the soil materials  for  them  are  the  loess  loams,  on  the  foothill  plains  –  the  binomial  loamy-cobble (pebble)  alluvial-proluvial  and  deluvial-  proluvial  drifts.  The  deluvial-proluvial   drifts  are  the pebble or cobble-loamy on the top and are underlain with the pebble or cobble.

E.2.3 Soil Quality

77.             The  baseline  environmental  examination  of  the  Kazakhstan  environmental  team included sampling of soils (OVOS). Environmental examination was implemented in 38 points at every 1 km along the Project Road. Chemical components covered by the study include 5 main substances: copper, zinc, lead, manganese, and arsenic.

78.             Heavy metal concentrations  in soils are shown in Table -7. Results indicate that for each  sampling  location.  The  highest  concentrations  of lead  were  obtained  at km 705  (22.9 mg/kg) in the vicinity of the city of Shymkent with operating petrol stations along the road; at km

714 (25.2 mg/kg) and at km 722 (23.4 mg/kg) both situated close to the half-damaged irrigation

channels.     Nevertheless, concentrations of lead in soil at all sampling locations did not exceed the MAC accepted in Kazakhstan maximum limit of 32 mg/kg for soils, although may still pose risks to human being as well as the environment.

Table -7 Results of soil sampling along the Project Road compared with approved MAC

in soils according to the local standards

| Sampling points along the road (km) | Main pollutants mg/kg |
| --- | --- |
|  | Cupric (flexible form) | Zink (gross form) | Lead (gross form) | Manganese (gross form) | Arsenic (gross form) |
|  | Test results | MAC | Test results | MAC | Test results | MAC | Test results | MAC | Test results | MAC |
| 705 | 0.042 | 3.0 | 0.09 | 23.0 | 22.9 | 32.0 | 496 | 1500 | <1.0 | 2.0 |
| 706 | 0.038 | 3.0 | 0.085 | 23.0 | 21.4 | 32.0 | 493 | 1500 | <1.0 | 2.0 |
| 707 | 0.034 | 3.0 | 0.091 | 23.0 | 19.6 | 32.0 | 476 | 1500 | <1.0 | 2.0 |
| 708 | 0.029 | 3.0 | 0.082 | 23.0 | 18.9 | 32.0 | 482 | 1500 | <1.0 | 2.0 |
| 709 | 0.022 | 3.0 | 0.091 | 23.0 | 14.7 | 32.0 | 387 | 1500 | <1.0 | 2.0 |
| 710 | 0.027 | 3.0 | 0.08 | 23.0 | 16.7 | 32.0 | 405 | 1500 | <1.0 | 2.0 |
| 711 | 0.024 | 3.0 | 0.061 | 23.0 | 16.2 | 32.0 | 410 | 1500 | <1.0 | 2.0 |
| 712 | 0.026 | 3.0 | 0.066 | 23.0 | 17.1 | 32.0 | 442 | 1500 | <1.0 | 2.0 |
| 713 | 0.029 | 3.0 | 0.087 | 23.0 | 16.1 | 32.0 | 391 | 1500 | <1.0 | 2.0 |
| 714 | 0.033 | 3.0 | 0.09 | 23.0 | 25.2 | 32.0 | 399 | 1500 | <1.0 | 2.0 |
| 715 | 0.026 | 3.0 | 0.084 | 23.0 | 21.1 | 32.0 | 378 | 1500 | <1.0 | 2.0 |
| 716 | 0.031 | 3.0 | 0.088 | 23.0 | 22.4 | 32.0 | 420 | 1500 | <1.0 | 2.0 |
| 717 | 0.036 | 3.0 | 0.068 | 23.0 | 22.9 | 32.0 | 468 | 1500 | <1.0 | 2.0 |
| 718 | 0.03 | 3.0 | 0.074 | 23.0 | 20.7 | 32.0 | 413 | 1500 | <1.0 | 2.0 |
| 719 | 0.027 | 3.0 | 0.062 | 23.0 | 20.5 | 32.0 | 433 | 1500 | <1.0 | 2.0 |
| 720 | 0.032 | 3.0 | 0.068 | 23.0 | 17.8 | 32.0 | 448 | 1500 | <1.0 | 2.0 |
| 721 | 0.027 | 3.0 | 0.061 | 23.0 | 15.2 | 32.0 | 396 | 1500 | <1.0 | 2.0 |
| 722 | 0.032 | 3.0 | 0.092 | 23.0 | 23.4 | 32.0 | 359 | 1500 | <1.0 | 2.0 |
| 723 | 0.026 | 3.0 | 0.077 | 23.0 | 12.4 | 32.0 | 396 | 1500 | <1.0 | 2.0 |
| 724 | 0.034 | 3.0 | 0.079 | 23.0 | 16.2 | 32.0 | 423 | 1500 | <1.0 | 2.0 |
| 725 | 0.028 | 3.0 | 0.064 | 23.0 | 16.8 | 32.0 | 399 | 1500 | <1.0 | 2.0 |
| 726 | 0.028 | 3.0 | 0.071 | 23.0 | 17.8 | 32.0 | 432 | 1500 | <1.0 | 2.0 |
| 727 | 0.03 | 3.0 | 0.065 | 23.0 | 17.5 | 32.0 | 420 | 1500 | <1.0 | 2.0 |
| 728 | 0.034 | 3.0 | 0.063 | 23.0 | 18.6 | 32.0 | 413 | 1500 | <1.0 | 2.0 |
| 729 | 0.02 | 3.0 | 0.093 | 23.0 | 13.2 | 32.0 | 363 | 1500 | <1.0 | 2.0 |
| 730 | 0.029 | 3.0 | 0.089 | 23.0 | 15.4 | 32.0 | 419 | 1500 | <1.0 | 2.0 |
| 731 | 0.022 | 3.0 | 0.083 | 23.0 | 13.3 | 32.0 | 386 | 1500 | <1.0 | 2.0 |
| 732 | 0.031 | 3.0 | 0.085 | 23.0 | 14.4 | 32.0 | 401 | 1500 | <1.0 | 2.0 |
| 733 | 0.029 | 3.0 | 0.08 | 23.0 | 12.9 | 32.0 | 488 | 1500 | <1.0 | 2.0 |
| 734 | 0.034 | 3.0 | 0.059 | 23.0 | 17.3 | 32.0 | 483 | 1500 | <1.0 | 2.0 |
| 735 | 0.027 | 3.0 | 0.052 | 23.0 | 14.3 | 32.0 | 441 | 1500 | <1.0 | 2.0 |
| 736 | 0.037 | 3.0 | 0.057 | 23.0 | 13.5 | 32.0 | 490 | 1500 | <1.0 | 2.0 |
| 737 | 0.028 | 3.0 | 0.094 | 23.0 | 11.6 | 32.0 | 396 | 1500 | <1.0 | 2.0 |
| 738 | 0.032 | 3.0 | 0.089 | 23.0 | 11.4 | 32.0 | 422 | 1500 | <1.0 | 2.0 |
| 739 | 0.024 | 3.0 | 0.091 | 23.0 | 11.5 | 32.0 | 390 | 1500 | <1.0 | 2.0 |
| 740 | 0.045 | 3.0 | 0.062 | 23.0 | 15.9 | 32.0 | 482 | 1500 | <1.0 | 2.0 |

| Sampling points along the road (km) | Main pollutants mg/kg |
| --- | --- |
|  | Cupric (flexible form) | Zink (gross form) | Lead (gross form) | Manganese (gross form) | Arsenic (gross form) |
|  | Test results | MAC | Test results | MAC | Test results | MAC | Test results | MAC | Test results | MAC |
| 741 | 0.04 | 3.0 | 0.040 | 23.0 | 12.7 | 32.0 | 401 | 1500 | <1.0 | 2.0 |
| 742 | 0.031 | 3.0 | 0.031 | 23.0 | 13.7 | 32.0 | 433 | 1500 | <1.0 | 2.0 |

Source:  OVOS.  Data  on  MAC  was  taken  from  “Sanitary  and  Epidemiological  Requirements  for

Atmospheric Air in Urban and Rural Areas, Soils and Their Protection, Maintenance of the Territories of

Urban and Rural Settlements, Working Conditions with Sources of Physical Impacts Affecting People", dated January 25, 2012

79. 	The highest concentrations of 0.042 mg/kg and 0.045 mg/kg for copper (flexible form) were  obtained  at  sampling  point  at  km  705  and  km  740  respectively  located  close  to  the electricity lines; the lowest concentration  was 0.2 mg/kg at km 729, with most of samples not exceeding  the MAC limit of 3 mg/kg. The concentrations  of other sampled contaminators  like zink, manganese and arsenic are also within accepted limits of Kazakhstan standards for soils.

E.2.4 Hydrology

80. 	Overview. Hydrographical network on the territory of South Kazakhstan is distributed unevenly.   River network  is more developed  in the mountainous  part of the territory.  On the plains it appears weak and is mostly represented  by transit rivers and temporary  waterways. The Syrdarya River, the basin of which includes all other rivers, occupies the central place in the hydrography of this area. The Syrdarya River has inflows only on the right side which begin in the  Western  Tien  Shan  ridges.  The  largest  of them  which  reach  the  Syrdarya  River  is the Chirchik River (with inflows Chatkal, Pskem, and Ugam), Keles and Arys (with inflows Borolday and Badam). The main source of supply for all rivers of South Kazakhstan, including the underground  waters,  is the water  from  melted  snow  and  rain  water,  volume  of which  does determine the volume of the annual flow.

81.             Project  Area.  The  Project  Road  does  not  cross  any  river.  However,  the  closest surface water sources to the starting point of the Project Road are the River Badam (2 km from the start point of the Project Road), River Keles (about 16 km from the end point of the Project Road) and Badam water reservoir (about 20 km from the Project Road). The Badam River is a left tributary  of the Arys River and originates from the slopes of the Badam  mountains.  There are two water reservoirs in the basin of the river. The water from the Badam River serves as a source  for irrigation  and domestic  needs. Pollution  of  the  river  is  mostly  due  to run-offs  of river valleys, farmlands, abandoned cattle   farms   and   some industrial    sites.   The   Badam water reservoir was built in 1974 for irrigation purposes its usable capacity is 61.5 million cubic meters.   Currently Badam  water  reservoir is  used  for irrigation  of  more  than  90 thousand hectares of fields. Situated within the Project Area Irrigation network is in the form of canals and aryks (irrigation ditch).

E.2.5 Water Quality

82. 	Project Area. Surface  waters in the Project Area are reported  to be monitored  by local agencies (Aral-Syrdarya Water Basin Management Unit and Sanitary-Epidemiological  Unit of South-Kazakhstan region) that provided the following information about the Badam river contamination.  According to the last data on the results of chemical analysis measured by two hydro-stations,  located  in  the  city  of  Shymkent  and  Karaspan  village,  the  main  identified pollutants are sulphates, nitrates, copper and magnesium.

E.2.6 Groundwater

83. 	Overview. The Republic of Kazakhstan is reportedly rich enough in groundwater  to fully satisfy the population with domestic, potable, technical and other waters in accordance with the needs of the population, industry and agriculture - but its distribution is extremely uneven. Quality  and  reserves  of  ground  water  vary  considerably.  Roughly  half  of  the  groundwater resources are concentrated in the south.

84.             Groundwater  is mainly belongs to the subterranean  waters of the quaternary alluvial sediments. The thickness of the alluvial sediments varies within the range of 7 - 24 m. Depending

on the lithological composition of the water saturated formations the discharge rates of wells vary within  the  range  from  1-2  to  10-15  dm3/s.  The  greatest  discharge  rates  are  typical  for  the formations  bedded  by the gravelly  pebble  stone;  the lowest  discharge  rates  characterize  the sandy  deposits.  The  waters  are  the  alluvial  sulphate-hydrocarbonate   sodium  with  1  g/dm3 salinity.

E.2.7 Air Quality

85.             The  baseline  environmental  examination  of  the  Kazakhstan  environmental  team included  air  sampling  (OVOS).  Environmental  examination  was  implemented  in  20  points located in 20 meters distance from the road axis at every 2 km along the Project Road in the vicinity  of  the  settling  areas.  Chemical  components  covered  by  the  study  include  4  main substances: dust, nitrogen dioxide, sulphur dioxide and carbon monoxide.

86.             The results  of the air examination  are provided  in Table  -8. There is a high dust pollution along the road with the highest concentration  of inorganic dust registered at km 731 (0.3 mg/m3) that is almost equal to the acceptable one-time maximum allowable concentration (MACot). One of the possible causes of the high level of dust could be agricultural machineries freely using the highway  and passing  it elsewhere  or driving  along the adjacent  to the road ground ways (based on personal observations made during the field surveys).

Table -8 Air quality analysis along the Project Road compared with approved MACot  in air according to the local standards

| Sampling points along the road (km) | Main pollutants mg/m3 |
| --- | --- |
|  | Inorganic dust | Sulphur Dioxide | Nitrogen Dioxide | Carbon Monoxide |
|  | Test results | MACot | Test results | MACot | Test results | MACot | Test results | MACot |
| 705 km | 0.24 | 0.3 | - | 0.5 | 0.033 | 0.085 | 1.26 | 5.0 |
| 707 km | 0.21 | 0.3 | - | 0.5 | 0.027 | 0.085 | 0.48 | 5.0 |
| 709 km | 0.26 | 0.3 | - | 0.5 | 0.038 | 0.085 | 1.74 | 5.0 |
| 711 km | 0.22 | 0.3 | - | 0.5 | 0.022 | 0.085 | 1.17 | 5.0 |
| 713 km | 0.26 | 0.3 | - | 0.5 | 0.037 | 0.085 | 0.69 | 5.0 |
| 715 km | 0.2 | 0.3 | - | 0.5 | 0.033 | 0.085 | 0.68 | 5.0 |
| 717 km | 0.27 | 0.3 | - | 0.5 | 0.041 | 0.085 | 1.34 | 5.0 |
| 719 km | 0.25 | 0.3 | - | 0.5 | 0.024 | 0.085 | 0.48 | 5.0 |
| 721 km | 0.21 | 0.3 | - | 0.5 | 0.028 | 0.085 | 0.6 | 5.0 |
| 723 km | 0.21 | 0.3 | - | 0.5 | 0.022 | 0.085 | 0.58 | 5.0 |
| 725 km | 0.26 | 0.3 | - | 0.5 | 0.031 | 0.085 | 0.81 | 5.0 |
| 727 km | 0.2 | 0.3 | - | 0.5 | 0.032 | 0.085 | 0.7 | 5.0 |
| 729 km | 0.2 | 0.3 | - | 0.5 | 0.032 | 0.085 | 0.9 | 5.0 |
| 731 km | 0.3 | 0.3 | - | 0.5 | 0.014 | 0.085 | 0.38 | 5.0 |
| 733 km | 0.22 | 0.3 | - | 0.5 | 0.028 | 0.085 | 0.43 | 5.0 |
| 735 km | 0.25 | 0.3 | - | 0.5 | 0.026 | 0.085 | 0.5 | 5.0 |
| 737 km | 0.24 | 0.3 | - | 0.5 | 0.029 | 0.085 | 0.56 | 5.0 |
| 739 km | 0.21 | 0.3 | - | 0.5 | 0.03 | 0.085 | 0.43 | 5.0 |
| 741 km | 0.21 | 0.3 | - | 0.5 | 0.034 | 0.085 | 0.68 | 5.0 |
| 742 km | 0.26 | 0.3 | - | 0.5 | 0.034 | 0.085 | 0.7 | 5.0 |

Source: National Kazakhstan EIA (OVOS). Data on MAC was taken from “Sanitary and Epidemiological

Requirements for Atmospheric Air in Urban and Rural Areas, Soils and Their Protection, Maintenance of the Territories of Urban and Rural Settlements, Working Conditions with Sources of Physical Impacts

Affecting People", dated January 25, 2012

87.             The  level  of  concentration  of  Sulphur  Dioxide  in  air  was  so  low  that  it  wasn’t registered by the used field equipment. The other components’ concentrations were obtained at sampling points not exceed accepted limits of Kazakhstan standards for air quality.

E.2.8 Climatic Context

88. 	Project Area.  The base data for the climatic characteristics  of the Project Area has been obtained from the long-term statistical records of different meteorological stations in South Kazakhstan region (Table -9) for the nearest of these station, Shymkent.

Table -9 Climatic characteristics

| Climatic Parameters, units | Shymkent |
| --- | --- |
| Average annual temperature, 0С | +11.9 ˚С |
| Absolute recorded maximum temperature, 0С | +44 ˚С |
| Absolute recorded minimum temperature, 0С | -34 ˚С |
| Depth of soil freezing | 14 mm |
| Average amount of precipitation | 455 mm |
| Width of snow cover | 10 cm |
| Mean annual wind speed, m/sec | 2-3 м/s |

Source: Project documentation (local EIA) provided by Road Committee of South- Kazakhstan region

89.             The Project Area located within South-Kazakhstan  region that can be characterized by sharply continental climate conditions. Summer is very hot, lengthy and dry, with precipitation inadequate for the natural growth of green plants.   Warm period lasts for about eight months- from mid-March  to mid-November.  The hottest month is July with an average temperature  of

29,5оС.  Daytime  can reach 37оC and at nights it drops to 20 оC. Occasionally,  during some

years, the absolute maximum temperature may reach +49 оС.

90.             The  winter  is  warm  and  short  –  about  3  months,  from  mid-December  to  mid- February- with frost rare, but the majority of days is sunny, frequent thaw, and snow-less. Snow- storms happen very rarely. Repetition of strong winds (over 15 m per second) is also limited. The lowest  temperature  may be noticed  in January  with an average  monthly  value of -6 оC. Night air temperature falls up to – 11 оC. The absolute minimum reaches– 40 оC.

91.             Stable snow coverage in this area is not recorded, though some years were noticed to be snowy. The average height of the snow does not exceed 1-2 sm. The number of foggy days is also insignificant. It makes only 20 days a year, and not more than 33 days in some of the years. More frequently fog happens in winter, but in average it does not exceed 6 days a month, with a maximum of 14 days a month.

92. 	Thunderstorms  on  the  subject  area  are  registered  year  round.  More  frequently thunderstorms are observed in summer – average of 3 days a month, and in anomalous years -

10 days a month. Thunderstorms are not observed only in December and January.

93.             In general, high level of the solar radiation, severe summer temperature  of the air, high level of relative humidity, absence of the atmospheric precipitates and frequent dust storms typical for this area create extremely difficult life conditions. The wind regime is illustrated below in the Table -10.

Table -10 Wind regimes (Shymkent meteo station)

| Directions and repetition of wind |
| --- |
| January |
| N | NE | E | SE | S | SW | W | NW | No wind |
| 5 | 11 | 32 | 14 | 4 | 6 | 11 | 17 | 26 |
| July |
| N | NE | E | SE | S | SW | W | NW | No wind |
| 7 | 19 | 25 | 9 | 4 | 6 | 12 | 18 | 19 |

Source: National Kazakhstan EIA (OVOS)

E.3 Social and Economic Environment

E.3.1 Administrative Organization

94. 	Overview.  The  Project  Area  is  located  in  South  Kazakhstan  region,  one  of  14 administrative   regions  of  Kazakhstan.  There  are  11  rural districts  and 4  cities of  regional importance, 7 cities (except Shymkent),  875 rural  settlements  in the region.  Each  region  and district and most urban settlements have their own elective councils, charged with drawing up a budget   and  supervising   local  taxation.   The  president   appoints   the  heads   of  the  local administrations  (known  by the Kazakh  term  akim)  and has the power  to override  or revoke decisions taken by local councils; an akim has the power to control budgetary decisions and to appoint the members of his staff, who are the department  heads of the jurisdiction.  The akim also can reverse budgetary decisions of the local councils.

Project Area.  The Project Road passes through four sub-administrative  territorial units of South- Kazakhstan region, in particular:

    Section km 705 – km 713 (8 km) passes through Shymkent city;

    Section km 713 – km 728 (15 km) passes through Sairam district;

    Section km 728 – km 737 (9 km) passes through Tole bi district;

    Section km 737 – km 745 (8 km) passes through Kazygurt district.

E.3.2 Economic Resources

95. 	Overview. Project Road passes through the territory of the South-Kazakhstan  region that social and economic development is based on both agricultural and industrial resources. Manufacturing  industries are the most promising ones in the region making about 67.0% of the total industrial   production. 38.4% of the  manufacturing   industry belongs   to food  processing,

11.1%  to  metallurgical   industry,  8.4%  to  manufacture of  peat  coal  and  5.3%  to  refined

petroleum products and production of pharmaceutical products.

96.             No  industries  are  reported  in  the  immediate  Project  Area.  However  there  are agricultural lands situated along the Project Road. Agriculture plays important role in social and economic    development     of    the    region.    During    the    year    (2010) local    enterprises produced 7.8 tons - of meat of cattle,  pigs,  sheep,  goats  and horses, 91.4 thousand  tons  - of cotton   fibber. Gross   value of agricultural   production is 163.8 billion   while   the   share of the national volume - 11.4% (Table -11).

97.             The     total     sown     area of     crops     in     the     region increased     by     8.7% (697.2 thousand hectares)  in  2010  compared with  the  previous  year. However  cotton  fields decreased by 2.0% in 2010 amounted to 137.3 thousand hectares.

98.             Project Area.  Economic resources in the immediate vicinity of the Project Area are primarily those that support dry land farming, an irrigation network and the grazing potential of the area's pasturelands. No minerals are known to be exploited in the immediate Project Area. The nearest quarries exploited for construction materials are located at conservable distances to the east and west of the Project Road. No industries or food processing facilities are known to exist in the Project Area.

Table -11 Production, investment and transport

| (Millions of Tenge unless otherwise noted) |
| --- |
| Industrial Production | Total Agricultural Production | Crop Production | Livestock Farming Production | Volume of Provided Services | Capital Investments | Turnover of Cargo Transport mil. Tonn km | Turnover of passenger Transport. Mil. pas-km |
| 316, 357.7 | 163,832.8 | 85, 152.3 | 77, 734.0 | 38,897.5 | 262, 595 | 4, 510.0 | 7 913,3 |

Source: Department of Statistics of South Kazakhstan region, accessed in January 2011 (http://www.

ontustik.stat.kz)

E.3.3 Transport Infrastructure

99.             Project Area.  The Shymkent – Tashkent Project Road is a link is the major element within   the  regional   transport   system.   The   Project   Road   represents   the   main transport link connecting Kazakhstan   with the  Middle  East  and  South Asia  through Uzbekistan.   The nearest  international airport  is located on the territory of Uzbekistan  in Tashkent  about 80 km from the Project Road. The nearest domestic airport is located in the city of Shymkent about 12 km  from the  Project  Area. The  railway  Shymkent-Arys-Tashkent  passes  on  the  west  at  a distance  of more  than 35  km from  the  starting  point  of  the  rehabilitated  road. There  is  no waterway situated close to or within the Project Road.

100.           In  addition  to  the  Project  Road,  the  most  significant  transport  features  in  the immediate  Project  Area  are  rehabilitated  grade  separated  interchange  at  km  732+963  and several  crossroads  with  adjacent  local  roads  linking  local  villages  with  regional  transport network.

E.3.4 Water Supply & Irrigation Systems

101. 	Overview.  Nowadays  only  482  settlements  of  total  900  of  the South  Kazakhstan region supplied with the drinking water that makes only 53.7% of the whole population of the region. Residents  of 247 localities use well water: 66 of which  is usually  taken from the open sources and 21 from the spring wells. Village dwellers of the past 13 settlements  continue to use  imported   water.   Project   Area.   The  Project   documentation   indicates   that  water   for construction possibly will be taken from the Badam River which passes through the city of Shymkent.  The drinking water for construction  camps is also proposed  to be drawn from the existing water supply system of the city of Shymkent.

102.           The  best  way  to avoid  any  shortage  of  the  local  water  resources  it to  establish autonomous water sources for the construction camps. According to information obtained from the regional Akimat, there are large amounts of underground water resources available for the local  water  supply,  but not all of them  have  been put into production.  In addition,  the local authorities include in these balances slightly saline waters that could still be used for various domestic and industrial purposes.

103.           Due  to  the  area's  limited  rainfall,  agricultural  production  in  southern  Kazakhstan relies heavily on the use of irrigation systems with water supplies derived from snow melts in the mountains. There is well developed irrigation network situated within Project Area. The Project will include the construction of installation or rehabilitation of 36 culverts.

E.3.5 Wastewater & Solid Waste Disposal

104. 	Overview.   The  total  length  of wastewater   and  drainage networks of  the  region is 754.6 km.  The  only  cities  are  supplied  with  centralized  wastewater  systems:  including in Shymkent 		(512.4 km      of      wastewater       channels), Arys (29.1 km      of      wastewater channels), Zhetysay (8.6 km    of   wastewater    channels),    Kentau (28.4 km    of   wastewater channels), Saryagash (13.5   km  of  wastewater   channels),   Lenger (66.5 km  of  wastewater channels), Shardara (49.7 km of wastewater  channels)  and the city of Turkestan (46.4 km of wastewater channels). All the networks belong to the communal ownerships of cities and most of them in a bad technical  condition  and need to be replaced.  The city of Shymkent  is the closest settlement with its own sewage system located on North of the Project Road.

105.           Project Area. Each town is reported to have an organization under the district Akimat which  is responsible  for collection  and disposal  of solid waste.  None  of these organizations extend solid waste collection services to the vicinity of the Project Road. However there some illegal waste can be observed along the road, especially close to the abandoned and damaged empty structures. In general the lack of the waste management  along the existing highway is visible and supported by the local people concerns.

E.3.6 Electrical Power, Pipelines & Other Utilities

106. 	Overview.  Electricity is  one  of  the  major  economic  sectors of  the  Project  located region. Energy enterprises produce  about 45-47% of  electricity needs of  the  region.  However South-Kazakhstan  itself is experiencing a significant shortage of electricity. The internal energy sources provide 45% -47% of the total local electricity needs, the rest are supplied mainly from the northern regions of the country through the power transmission lines with the power of 220 -

500 kV. Partly energy imported from the Kyrgyz Republic on the basis of an intergovernmental agreement on   the   integrated use   of the   Naryn-Syrdarya hydro   power   station. Electricity distribution Company Ontustik Zharyk transit LLC maintains an electrical network of 110 kV and below  with  the  total  length of  high  voltage overhead  and  cable lines  is 22,310 km.  About

21,730.987 km, of which are air power grids and 578.895 km is cable lines.

107.           Project Area. It is planed to rehabilitate in total 9 electricity lines of 10kV and 0, 4kV crossing the Project Road. There are five intersections with electricity overhead lines of 10kV. The planned rehabilitation includes replacement of old poles with new concrete ones.

E.3.7 Land Uses and Displacement Issues

108.           Project Area. Land uses along the Project Road are dominated by agriculture; mostly grazing (cattle, sheep, goats and herding of horses) and dry cash crops such as wheat and corn. Farm crops are mainly fodder plants, wheat and maize. Almost all homesteads in the rural areas have small horticulture  gardens  for growing  common  vegetables  for self consumption.  Some level of irrigated farming exists in the area as evidenced  by the fact that the Project includes plans to rehabilitate 36 irrigation pipes.

109.           There   are  also  some   structures   situated   along   the  road  within   fixed  ROW. Nevertheless  as  reported  by  the  head  of  the  RC  of  South-Kazakhstan  region  none  of  the existing structures situated along the road will be impacted or damaged during the construction of the Project Road.

E.3.8 Demographic Characteristics

110. 	Overview.   The  Project  Area  is  within  South  Kazakhstan   region  which  had  a population of 2.6 million people reported in January 2011 and a population density of about 22 people to km2. The urban population is 1.007.8 thousand people (39.3%) and rural population is 1,559.9 thousand people (60.7%). Gender statistics of the region can be described as follow, according to the    data    dated    to    January    2011, the    number    of    men in the    area is

1,269.405 thousand (49.4%) and women 1,298.302 thousand (50.6%).

111.           Project Area. Data on demographic  situation of the districts crossed by the Project

Road sections is provided by Table -12.

Table -12 Characteristic of population of the Project Area

| Administrative Unit | Population As of January 2011 | Born (January 2011), | Died (January 2011) | In- Migrants (January 2011) | Out- Migrants (January 2011) | Employed (January 2011) |
| --- | --- | --- | --- | --- | --- | --- |
| Shymkent | 629,100 | 16,600 | 4,063 | 11,751 | 10,735 | 126,300 |
| Tole bi district | 127,400 | 3,450 | 941 | 1,794 | 1,736 | 10,900 |
| Sairam district | 302,700 | 9,568 | 1,616 | 749 | 1010 | 44,139 |
| Kazygurt district | 105,500 | 3,275 | 618 | 500 | 1,353 | 51,876 |

Source: Retrieved from the Department on Statistics of South Kazakhstan region, Shymkent, 2012

E.3.9 Employment

112. 	Overview.  Industry  is  one  of  the  important  economic  sectors  in  the  region.  The number of economically  active people of South Kazakhstan  region is 1.091 thousand people. About 449 of economically active people are living in the cities. The number of employed people in 2011 has increased to 337.5 thousand people. The number of unemployed people amounts to 68.4 thousand people. The current level of unemployed in the region is 5.9%. The number of economically  inactive people (e.g., school pupils, students, householders,  retirees and disable

people) is 465.7 thousand  people with rate of economically  passive people equal to 28.6 %. Statistical data on relevant to Project Area districts is given in Table -13.

Table -13 Employment in the Project Area

| Administrative Unit | Employed (December of 2011) number of people | Hired Workers (Percent) | Unemployment Rate (Percent) |
| --- | --- | --- | --- |
| Shymkent | 126,300 | 52.4 | 5.4 |
| Tole bi district | 10,900 | 52.4 | 5.7 |
| Kazigurt district | 9,400 | 52.4 | 5.8 |
| Sairam district | 32,100 | 52.4 | 5.1 |

Source: Department on Statistics of South Kazakhstan region

E.3.10 Employment  Ethnic & Vulnerable Groups

113. 	Overview. Native Kazakhs, a mix of Turkic and Mongol nomadic tribes, migrated into the area now known as Kazakhstan region in the 13th century and remain the country's largest ethnic group. The Kazakh steppes joined to Russia in the 18th century. Kazakhstan became a Soviet  Republic  in  1936.  During  the  1950s  and  1960s  agricultural  "Virgin  Lands"  program, Soviet citizens were encouraged to help cultivate Kazakhstan's northern pastures. This influx of immigrants  (mostly  Russians,  but also  some  other  deported  nationalities)  altered  the ethnic mixture and enabled non-Kazakhs  to outnumber natives. Independence  in 1991 caused many of these newcomers to emigrate. The 2009 Census reported South Kazakhstan region's ethnic groups as follows:

Kazakh (70.2%) 	Tadjiks (1.17) 	Kurds (0.34%) Uzbek (17.50%) 	Tatars (0.88%) 	Ukrainians (0.33%) Russians (5.96%) 	Turks (0.87%) 	German (0.15%) Azerbaijanis (1.26%) 	Koreans (0.40 %) 	Other (0.9%)

114.           The  population  of  the  region  differs  from  the  national  averages  with  a  larger percentage of Kazakhs and a significantly smaller number of Russians. Project Area.  Within the immediate vicinity of the Project, the resident population is extremely small and predominantly Kazakh.  Most of the residents of the rural areas follow the Muslim religion.

115.           Overview.   The  standard  of  living of  the  population in  2010 is  characterized   by the key  indicators  of  nominal real incomes per  person,  which  in the  South-Kazakhstan was amounted to KZT 25,037 per month, while monthly average expenditures was KZT 15,420 per capita.  Percentage  of  population below  the  poverty  level in the  area is  11.5%  of  the  total population. The level of standard of living of the South-Kazakhstan  population in 2010 is given in Table -14.

116.           There  has  been an  increase  of income  per  capita in the  whole  region  when the higher     income was     recorded in     Shymkent,     Arys     and Suzak cities     in    the     recent years. Lowest income per capita was indicated in Kazygurt and Saryagash districts. There are more   than 39.6   thousand Second   World   War   veterans   and persons   equated   to   them, including 1,492 disabled  people  and  participants  of the  Second  World  War,  as  well  as more than 113 thousand mothers of large families, which is 5.47% more than in 2008 and 603 elder people living alone (older than 80 years) in the South-Kazakhstan region.

E.3.11 Health Facilities and Public Health Issues

117. 	Overview. Following its appointment as a member of the World Trade Organization (WTO), Kazakhstan has brought its local medical regulations in line with international standards. A  program  of  reforming   and  development   of  public  health  has  been  approved   by  the Government.   Its main measures  include  plans to increase  public health expenditure  to four percent  of  GDP  by  2010.  In  keeping  with  this  national  policy,  the  region  and  district  level healthcare institutions are being restructured from being purely public to being semi-private institutions.

118.           There  are  well  developed  medical  infrastructure  in  the  South-Kazakhstan  region consists  with 120 hospital  organizations, including  43 rural hospitals;  250 policlinics, including

29 clinics,  24 primary  health  care centres;  168  treatment  policlinics  and  539 health  centres.

Project Area. The closest large medical facilities to the proposed ROW located in the largest regional  city  of  Shymkent.  However  there  are  also  district  level  polyclinic  in  Rabat  with  2 emergency cars and some medical posts usually served by 1 or 2 people in all villages.

Table -14 Indicators of living standards in South-Kazakhstan region

| Name of the indicator | Units |  |
| --- | --- | --- |
| Nominal and real income, the monthly average per capita | KZT | 25,037 |
| Percentage of population with incomes below the subsistence minimum | % | 11.5 |
| The growth rate of the population with incomes below the subsistence minimum | Thousand people | 451.1 |
|  | % | 98.3 |
| The index of real income | % | 109.2 |
| Monthly expenditure per capita | KZT | 15,420 |
| Consumer spending | KZT | 14,705 |

Source: Department on Statistics of South Kazakhstan region

E.3.12 Local Education Facilities and Amenities

119. 	Overview.  Primary and secondary  education  in Kazakhstan  consists in three main educational  phases:  Primary  education  (forms 1-4); Basic general education  (forms 5-9) and Senior level education (forms 10-11 or 12) divided into continued general education and professional education.

120.           In South Kazakhstan  region, as in other regions  of Kazakhstan,  public secondary education    is    mandatory    for    all    children    under    18    years    of    age.    There    were

530.6 thousand students   registered   in 2011   -   2012 school year   in   the South   Kazakhstan

region. According to National Statistical Agency, for January 2011, 99.0% of schools in South- Kazakhstan region are computerized, 93 percent of schools connected to telephone land lines, and  85 percent  of schools  have  access  to internet.  In the field of 92 institutions of technical and vocational training is carried  out on 90 specialties in the number  of 77,227 people. There are 93 after school education  institutions. The overall employment rate is about 97%. Most of higher education institutions are located in Shymkent.

121.           Project Area. No local education facilities or amenities are known to be located in the Project Area. The closest are believed to be located in the city of Shymkent and some other villages located close to the road (like Akzhar, Aktas, Rabat and village after K.Mambetov (Mambetov)).

E.3.13 Human Trafficking

122. 	Overview. There is considerable  flow of labour migrants from Uzbekistan to South- Kazakhstan region or through it to other parts of Kazakhstan, mostly illegally working in the construction sector. There are several NGO assisting migrants and working against human trafficking, like the Legal Centre for Women's Initiatives "Sana Sezim" and Public Association “Bereke” in South-Kazakhstan based in the city of Shymkent.

123. 	NGO   Sana   Sezim   has   well-developed   organisation   structure   (Figure-7)   and cooperation links with other relevant organisation working on protection of human rights. Among one  of  the  recent  projects  implemented  by  NGO  in  December  2011    – December  2012  – “Providing  legal  assistance  to  migrant  workers  from  Uzbekistan”  supported  by  Embassy  of Norway in Kazakhstan.

E.3.14 Cultural Resources

124.           Overview.  South Kazakhstan  region is one of the valuable  historical  places of the

Republic  of  Kazakhstan.  It  has  many  historical  and  architectural  monuments.   There  are

33 monuments of the material and spiritual culture of national importance and 434 sites of local importance registered in the South-Kazakhstan region. Project Area. However there are no resources of cultural or historical importance situated within the Project Area except newly established monument called Noah’s Ark. This modern monument is located up on one of the Kazygurt hills and it has panoramic area around it. There are arranged road access from the highway to a built-up parking area and pedestrian walkways supported by stairs. Nowadays monument  is one of the popular places to visit among young people living in Shymkent  and some other villages located along the Project Road.

E.3.15 Public Safety

125. 		Overview. According to the State Committee on Legal Statistics and Special Records of South-Kazakhstan  region in 2010, the number of reported crimes amounted to 10.331 cases in the region. Among the most common types of crimes are crimes against property. The share of female persons committing crimes  in 2010  was 12.2% (in 2000 - 13.0%), including  females under 	the    18    year -    7.8% (in    2000    9.0%). The    unemployed population    accounted for 84.0% (85.0%) of all identified offenders of the crime.

126.           As  reported  by  NGO  Sana  Sezim,  domestic  violence  against  women  seems  a general problem. Most of the case linked with women impacted by human trafficking.

Figure -7 Working structure of NGO Sana Sezim

Source: Official web-site of NGO Sana Sezim http://sanasezim.org

F. ANTICIPATED ENVIRONMENTAL IMPACTS AND MITIGATION MEASURES

127.           The planned rehabilitation of the Shymkent-Tashkent  road had been classified as a Category B project under the provisions of ADB Safeguards Policy Statement (July 2009), which means that no significant and irreversible impacts are expected as a result of the proposed interventions.  This initial classification  coincides  with the results of the regional  assessment, which  confirms  that  the  relevant  environmental  issues  will  mainly  relate  to  the  construction period.

128.           While the project will also involve upgrading of the first 37 km of the existing road, this will be undertaken within the existing ROW and will not impact on any critical areas. Further, this road section is located close to Shymkent where he environment already impacted by anthropogenic activity. As such, the expected project impacts will be largely experienced during the construction phase and are considered temporary. However some potential impacts need to be taken into consideration during the Pre-Construction Phase.

F.1 Pre-Construction Phase

F.1.1 Design Project

129.           Since, this is an existing road and proposed for rehabilitation the same alignment will be followed with required geometrical improvements and widening of the road. The road design follows the highway road construction standards of Kazakhstan. The visual appearance of the landscape  along  the  Project  Area  will  change  to  some  extent  because  of  construction  of structures such as (elevated) embankments, culverts, crossway passages, roadside plantations etc.

130.           Visual changes to the topography will be of permanent and minor negative in nature and  do  not  require  mitigation  measures,  except  that  the  Project  design  should  consider aesthetic  concerns.  The latter refers particularly  to roadside  plantations  and re-installation  of borrow sites.

F.1.2 Pedestrian Crossings

131.           Due to the planned change of the road speed and presence of public using facilities like bus stops along the road it is important to condiser pedestrian safety early on the pre- construction  phase.  Absense  of  adequate  installation  of  bypassing  facilities  together  with warning  signage  might  cause  increase  of  road  accidents  and  impact  on  development  of negative perception of the International highway by local population.

132.           Generally, the Design makes provisions for bypassing the highway traffic to ensure that  local  residents  do  not  come  in  direct  contact  with  traffic  movements.  Bus  stops  near settlements  are planned  on the side  of carriageway  where  most  people  would  access.  The warning  signage  and  speed  limits  are  included  at  all  sections  where  pedestrian  crossing facilities are planned. Pedestrian crossings need to incorporate structures that allow the use of prams, wheelchairs, bicycles and pushcarts.

F.1.3 Local Animal Passages

133.           Domestic animals are observed at certain sections of the road corridor, particularly in the vicinity of human settlements, and this fact may impact the road safety. Road accidents can be caused by livestock unexpectedly passing the highway.

134.           There  are  four  existing  animal  crossings  functionally  combined  with  agricultural machinery  passages  situated  along  the  Project  Areas  that  have  to  be  rehabilitated  with preservation of its’ geometry or widening of the narrow ones. The Design also includes establishment of adequate fencing near the animal crossings on both sides of the road.

F.1.4 Removal of Roadside Vegetation

135.           Roadside  shelterbelt  areas are a rare and valuable  natural  asset in the generally uniform  steppe  landscape  dominating  the road corridor.  Because  of their intrinsic  ecological

benefits and values, roadside plants (especially large bushes and trees) should be maintained to  the  maximum  extent  possible,  as  they  act  as  natural  barriers  absorbing  sand  and  dust impacts. Roadside plantations  will also contribute to a year-round  aesthetical  improvement  of the landscape. Both authorized and un-authorized cutting of roadside trees will affect the overall ecological properties in the Project Areas.

136.           However, the impact will be medium-termed and moderate, as long as the plantation of new trees is integrated in the Design documentation  as reported by local OVOS. In addition to this it worth to consider the fact that none of new trees should be palatable for local grazers. Import  of exogenous/alien  plant  species  for plantation  shall be strictly  forbidden.  During  the detailed  design  a cutting plan will be prepared  and included  in the contract  specifications.  It needs  to  be  approved  by  the  responsible  agency,  the  Regional  Units  of  the  Ministry  of Agriculture’s  Forestry  and  Hunting  Committee  (CFH)  in  Shymkent.  The  Contractors  will  be required to limit cutting and pay strict attention to the detailed design measure and consult with CFH.

F.1.5 Site Selection of Work Camps and Facilities

137.           The  location   of  the  Constructor’s   camp  site  is  often  crucial   in  planning   for environmental  safeguards,  particularly  in view of protecting  the public general as well as the work force from adverse impacts, nuisances and health hazards. Unappropriate  siting of work camp and material stores, together with bringing of outside labor, may cause encroachment of agriculture land, alteration of drainage, solid waste and waste water problems. In addition, the location of construction  camps within or in vicinity to an existing settlement (like in Shymkent, Aktas, Akzhar, Mambetov etc.) can result in a number of other impacts and conflicts, such as shortage and competition for amenities, food and water.

138.           The  National  Kazakhstan  EIA  (OVOS)  as  well  as  Design  documentation  make several assumptions and pre-selections of potential sites, but the final decision on selecting a location will depend on the Contractor and his logistic requirements.  The final site selection of the camp site and particularly the positioning of impact-generating  machineries like the Asphalt Mixing Plant, crushers and concrete batchers should follow a careful consultation  of the local wind  conditions,  in  order  to  choose  locations  that  are  always  in  sufficient  distance  on  the leeward side of the prevailing local winds. Locating of work camp sites or emission-generating machineries  and  yards  in a distance  shorter  than  500  m from  sensitive  spots  like  schools, hospitals and recreational facilities should be prohibitive.

139.           All  planned  and  ongoing  activities  associated  with  construction  camps,  including storage facilities, workers dormitories, sanitary instalments and safety measures are subject to the recommendations  presented  in the EMP. This is particularly  the case where construction camps  will  be  set  up  within  or  nearby  existing  settlements.    In  line  with  the  Kazakhstan legislative framework the principal tool to ensure an environmentally sound execution of all construction works, including the establishment for work camps and facilities, is the preparation of a site management  plan – in Kazakh terminology recognized as ‘Construction  Environment Action  Plan  (CEAP)’.  This  CEAP,  subject  to approval  by various  agencies,  is the  essential warrant that all work activities will be carried out in an environmentally sound manner, aiming at eliminating or minimizing potential impacts identified in the Kazakh EIA or in this document. Compliance will be strictly monitored by supervision engineers, and the Contractor will be held liable for any non-compliance.

F.1.6 Local Water Resources

140.           Construction works require large amounts of water, both for supply of drinking water for the labour forces and the operation of the camp sites, and for all technical purposes relating to construction activities. The required amounts may attain tangible volumes that may interfere with  local  water  resources,  and  thereby  bear  the  potential  for  interference  with  communal livelihood and needs.

141.           All Contractors have to submit a plan for type, location and quantity of both drinking and technical  water  extraction.  Non-approved  extraction  of large amounts  of water  from the local aquifer may also result in a number of secondary impacts, most of them prone to cause

ecological issues and social conflicts, as well as delays for the project. Therefore, the extraction plans need meticulously be observed and monitored, and require prior approval from local authorities.

F.1.7 Selection of Borrow Pits

142.           All  required  construction  materials  are  reported  in  available  in  sufficient  source quantities and qualities according to the Design documentation.  Reinforced concrete products and pre-cast structures (such as pipe culverts) and few more special road construction materials need  to be transported  from  the  city  of Shymkent.  However  there  is a still risk  of adverse impacts  like  accelerated  land  erosion,  landslides,  disturbance  in  natural  drainage  patterns, water logging and water pollution mostly could be linked with the need of establishment of new borrow pits.

143.          The selection and operation of borrow pits needs to be carried out with all due considerations  to avoid  any  impact  on the existing  natural  and  human  environment,  and  to make provisions that no secondary impacts such as soil and aquifer pollution will occur. In case where new hauling roads need to be constructed, the Contractors need to detail all particulars and  precautionary   measures  in  the  CEAP.  In  cases  where  hauling  roads  pass  through intensively used pasture land, protective animal fences need to be established along such roads to prevent collisions with local livestock. Special attention need to be given to the stockpiling of borrow  materials  to  avoid  spillage  of  sediments  into  nearby  terrain.  All  borrow  pits  and temporary hauling roads need to be re-instated into their former (close-to-natural) condition and appearance.

F.1.8 Cultural, Historical and Archaeological Assets

144.           Although  not identified  in the preliminary  survey of the Design  Company,  there is always a risk that earth works may encounter or damage existing structures of cultural, historical or archaeological value.

145.           In case of accidencial discovery of locally valuable cultural or historial structures the Contractor needs immediately inform the Engineer respectively representatives of the Archaeological Expertise Institute of Kazakhstan who then will advise on further and appropriate actions. Construction works are to be resumed only after written approval from this agency. The Contractor  shall  seek,  in close  consultation  with  the RE  and  the  relatives  of the  victim,  an amicable  solution in cases where a burial or memory sites (tombstone,  with or without small fence) is located within the RoW. Such tombs may be relocated for few hundred meters, as applicable and agreed by the family or representatives of the road victim.

F.1.9 Indigenous or Vulnerable People

146.           The Contractors  shall be obliged to pay special to common gender issues, and to overcome disproportional discriminations of women by the provision of sufficient and fairly-paid work  contracts.   There  is  also  potential  risk  of  human  trafficking,   often  associated   with construction projects, is equally addressed in the EMP.

F.2 Construction Phase

F.2.1 Potential Impacts on Public Access, Utilities and Services

147. 	As  the   rehabilitation   of  the   Project   Road   considers   replacement   of  existing engineering   infrastructure,   that   might   cause   impacts   to   local   services   associated   with construction works within or nearby local settlements. The Contractor has to be responsible for arrangement of continuous work of all local services and utilities that may potentially be affected by the construction works. This is particularly important in view of public utilities (water pipes, electric cables) which are planned to be removed due to widening the carriageway. All utilities subject to removal need to be fully replaced before disconnecting the existing utility.

148.           The best practice  for precaution  of any forthcoming  problems  with local residents include (i) timely public announcement of near-future planned construction activities (ii) strict observance  of working hours and speed limits as determined  in the Technical Specifications,

and  (iii)  involving  as  much  as  possible  local  residents  in  work  contracts  to  secure  their satisfaction and support.

149.           Any damage or hindrance/disadvantage  to local business caused by the premature removal or insufficient replacement of public utilities is subject to full compensation, all at the full liability  of  the  Contractor   who  caused  the  problem.  The  Contractor   shall  also  maintain unhindered  access and use of social, cultural and religious  sites (e.g. mosques,  cemeteries, cultural  gathering  places,  sports  facilities).  In  case  of  any  damage  of  private  properties, including   livestock   and  homestead   gardens,   the  Contractor   will  be  held  fully  liable   to compensate and rectify the inflicted damage.

150.           The presence of construction  camps may put additional problems for local utilities. Work Sites require  large and steady  amounts  of electricity,  which  may overburden  the local supply services. Local health services will be under possible pressure of large numbers of work force in the area that might require  additional  assistance.  Finally,  the close location  of work camps near settlements can possibly impair the entire social and cultural fabrics of the resident community  (e.g.  increase  of  air  and  noise  pollution,  social  conflicts,  crime  rates,  STDs, prostitution etc.).

151.           The Contractors/sub-contractors shall exert all efforts to maintain good relationship with the local residents, particularly while aiming at preventing noise and air pollution impacts, and avoidance of crime conflicts with the work forces.

F.2.2 Campsites

152.           Construction  camps  can  evoke  short  to  medium-term  impacts,  although  most  of these impacts are manageable and shall not interfere with the public life of nearby communities. Unappropriate  siting of work camp and material stores, together with bringing of outside labor, may cause encroachment of agriculture land, alteration of drainage, solid waste/ waste water problems, and spread of infections. In addition, the location of construction camps within or in vicinity to an existing settlement (like in Shymkent, Aktas, Akzhar, Mambetov etc.) can result in a number of other impacts and conflicts, such as shortage and competition for amenities, food and water.

153.           Although temporary and mostly moderate, construction-related  noise impacts in the vicinity of residential areas are likely to cause some health problems. The maximum allowable noise level of point sources shall not exceed 70 dBA. Of particular concern are noise levels in the vicinity of schools, kindergartens  and hospitals,  where noise levels should not exceed 10 dBA. The Contractor has to make all possible efforts to keep the noise production at the lowest possible level when carrying out his works in the vicinity of such sensitive spots.

154.           For establishment of work campsites, most if not all of the potential impacts can be set off by choosing a location in sufficient far distance from existing settlements, as long as electricity and water supply can be managed. One of the guiding principles for site selection is the alignment to the prevailing wind directions and consultation with local authorities.

155.           In  case  of  the  location  of  the  camp  site  near  settling  area  mitigation  measures against noise and vibration have to include, but are not limited to the following:

(i)  Selection of modern and well-serviced equipment and plants with reduced noise level ensured by suitable in-built techniques and appropriate silencing devices;

(ii)  Confining  excessively  noisy  work  and  movement  of  heavy  machinery  to  specified daytime working hours (this relates especially to stone crushers. percussion hammers and pneumatic drills);

(iii) Work hours need observe special restrictions near residential and sensitive areas; (iv) Providing the construction workers with suitable hearing protection (ear muffs);

(v) Avoid vehicle idling.

156.           Public   information   is  required   wherever   works   including   bulldozers,   scrapers, pneumatic hammers, crushers, loaders, and compaction loaders produce excessive noise and

vibration, to alert the public general for unavoidable noise development and the anticipated level of nuisance. As rule of good practice, no construction activity should be carried out near human settlements  that would exceed  90 dBA for more than one continual  hour. In case of proven damages  to infrastructure  (private  and non-private  assets)  the Contractor  is obliged  to seek friendly settlement of disputes and make ample provision for adequate compensation payment to the afflicted owners.

157. 	Unbalanced  driving  habits are the main sources  of vibration  impacts  on structural objects, including humans. As for construction machinery, good driving practices are within the obligations of the Contractor for guiding his work forces. Otherwise, road surface compaction, surface granule metric composition and speed control are proven means of containing such impacts.

158.           The working ambience must fulfil minimum and standard requirements  for ensuring healthy and safe work conditions, as prior defined in the CEAP. Mandatory mitigation actions include:

(i)  All contracted labour shall undergo a medical examination which should form the basis of an (obligatory)  health/accident  insurance and welfare provisions to be included in the work contracts. The Contractor shall maintain records of health and welfare conditions for each person contractually engaged.

(ii)  The contractor  shall seek his own electric supply system, preferably  separated  from the public grid.

(iii) After consulting with local Water Departments, the contractor needs to ensure his own water  supply  system  (supposedly   by  constructing   his  own  wells  for  drinking  water purposes.

(iv) As for use water, he needs to initiate tests by the specialized agency to determine the maximum allowable abstraction volume from local groundwater or any other water sources.

(v) The Contractor shall provide adequate and functional systems for sanitary conditions, toilet facilities, waste management, labour dormitories and cooking facilities. To the extent possible, he shall provide (import) food items for the workers to alleviate potential burdens from scarce local market resources.

(vi) The camp sites, and particularly the fuelling area, shall be equipped with the special wastewater  collectors combined with separator basins. The camp site needs to have its own sealed containers for sludge disposal from septic tanks.

(vii)The  problem  of  overburdening   the  local  health  facilities  can  be  best  solved  by establishing a well-equipped ambulance station at the camp sites, and to engage qualified medical personnel for the entire duration of the work phase. Such personnel should also be trained in conducting  regular awareness  campaigns  among the workers, focusing on the prevention and control of communicable diseases (e.g. HIV/AIDS) and drug abuses.

(viii)        The   camp   site   should   be   secured   against   unauthorized   access.   Special precaution measures are required for securing and storing hazardous materials.

159.           In order to ensure the safety of employees during the performance of their duties, it is suggested:

(i)     to provide all workers with work-specific protective clothing; (ii)     to provide sufficient hygiene supplies and sanitary facilities; (iii)    to prevent occupational diseases;

(iv)    to prevent communication of sexually transmittable diseases;

(v) 	organization of good rest and nutrition workers during working breaks; (vi) 	implementation of social benefits and guarantees.

160.           Each   contractor    will   be   requested    to   prepare    an   approved    Site-Specific

Environmental  Action  Plan  (SS  EMP),  which  will,  among  others,  delineate  all  work  safety

aspects he intends to apply. Focal points of the SS EMP will relate to means, type and number of protective clothing, safety precautions at specific work sites, first aid, rescue plans, and all intended measures for avoiding or proper clearance of hazardous substances, including fuelling operations, transport and handling of hazardous materials and explosives, securing measures etc.

161. 	Construction  works  and  activities  carried  out  in  workshops  bear  the  numerous accident and health risks for both the labourers and the public general, with varying direct and indirect consequences. Therefore, the SS EMP needs to make provision for specific medical services and provisions, workers insurance policies and indemnities, emergency provisions and a rescue/evacuation planning in case of major accidents.

162. 	The contractor will be obliged to hold, at regular intervals, training sessions with all work forces (including engineers and supervisors) that will address the following aspects:

(i)  General aspects on work safety and environmental awareness building; (ii)  Worker’s responsibilities in case of emergency and spills;

(iii) General work safety in relation to common work risks, demonstration  and use of protective equipment (first aid, fire extinguishers, handling explosives,)

(iv) Work hours and speed limits, environmentally harmful activities; (v) First aid assistance and medical assistance in emergency cases; (vi) Emergency/rescue action training, incl. use of towing equipment;

(vii)Rising  awareness  on the problem  of conveying  sexually  transmissible  diseases

(e.g. Syphilis and HIV/AIDS) between work forces and local residents;

(viii)  Avoidance of conflicts with local communities, maintaining good relationship with local residents and authorities;

(ix) Actions required in case of detecting archaeological or historical items during work.

F.2.3 Air Pollution

163.           Air pollution is known to cause a variety of health risks to both the workers and the general public. Dust will be major problem during the construction of the road. It is anticipated that impact on air quality will be direct, of low magnitude, local, reversible and short term.

164.           The Contractor should include necessary measures to reduce air pollution and dust development that would impact the public health, by:

(i)  provision of dust masks to operating personnel; (ii)  arrangement of regular water spraying;

(iii) equipping  of  asphalt,  hot  mix  and  batching  plants  with  fabric  filters  or  wet scrubbers to reduce the level of dust emissions;

(iv) provision of protecting canvasses obligatory for all trucks transporting material that could generate dust, and

(v) planning  of  access  roads  sufficient  distances  from  residential  areas  and,  in particular, from local schools and hospitals.

165.           Appropriate measures should be taken to limit or suppress exhaust emissions from construction  vehicles.  Construction  vehicles  and  machinery  should  be kept  in good  working order, regularly serviced and engines turned off when not in use. The Contractor should provide specific and regular training to all work personnel to ensure avoidance or minimization of the anticipated impacts associated with work operations.

166.           Vehicles  with  an  open  load-carrying  case  transporting  potentially  dust-producing material  shall have properly  fitting sides and tail boards.  Dust-prone  materials  should not be loaded to a level higher than the side and tail boards,  and should be covered  with a strong tarpaulin. In periods of high wind, dust-generating operations should not be permitted within 200

m of residential areas. Special precautions need to be applied in the vicinity of sensitive areas such as schools, kindergartens and hospitals.

167.           Unauthorized burning of construction waste material shall be subject to penalties for the contractor, and withholding of payment.

F.2.4 Surface and Groundwater Resources

168.           During construction surface and groundwater resources may be polluted by spoil and construction wastes. Rest areas and petrol filling stations are the principal locations where road users may contribute to pollution of water resources. Installation of suitable garbage containers, functional  public toilets  and appropriate  signage  at rest areas  are suggested.  Some surface water resources,  like local lakes, can be impacted by illegal fishing activities  that may cause wide range of negative outcomes from pollution to dissatisfaction with the local population.

169.           For the extraction of water for construction purposes, the intake from natural surface waters like the Badam or Keles Rivers will require prior permission of the responsible local authorities. The Contractors must equally give full attention to prevent any pollution of the river, input of excessive sediment loads or change of the natural flow, since the local population uses this river for domestic purposes. The contractor must control any illegal fishing activities by work forces, and shall strictly impose penalties on violators.

F.2.5 Borrow Pit Operations and Excavations

170.           Most of the construction materials are planned to be taken from existing functioning borrow  pit pre-defined  in the Design  documentation.  However  there is a still risk of adverse impacts  like  accelerated  land  erosion,  landslides,  disturbance  in  natural  drainage  patterns, water logging and water pollution mostly could be linked with the need of establishment of new borrow pits.

171.           If there will be need on establishment of a new one, Technical Specifications have to be  filled  with  guidance  to  Contractors  and  Sub-Contractors  on  the  opening,  operation  and closing of quarries and borrow pits. A site management plan will be required for each borrow pit operation.   While  the  contractor   will  be  sourcing   the  borrow   materials   under  their  own arrangement,  the  following  measures  to  minimize  impacts  associated  with  the  operation  of borrow areas shall be implemented:

(i) Secure all required environmental approvals and carry out extraction and rehabilitation activities consistent with the requirements of MOEP and/or permit conditions;

(ii)  Prior  to  operation  of  the  borrow  areas  submit  to  RC  and  construction  supervision engineer the following:

- a plan indicating the location of the proposed extraction site as well as rehabilitation measures  to  be  implemented  for  the  borrow  areas  and  access  roads  upon  project completion

- dust management  plan which shall include schedule  for spraying on access road and details of the equipment to be used

(iii)  Undertake   regular   dust  suppression   on  all  unpaved   access   roads  during  the construction period, particularly in sections where critical receptors, such as settlements, are located;

(iv) Locate stockpiles away from watercourses to avoid obstruction of flow and siltation; (v) Provide cover on haul trucks to minimize dust emission and material spillage;

(vi) Undertake repair of access roads to their original condition.

F.2.6 Specific Construction Activities

172.           The  operation  of  asphalt  mixing  plants  (AMP)  frequently  causes  a  number  of environmental   impacts.  Although  short  in  time,  the  corresponding   impacts  may  result  in substantial health risks for the public general and for the workers. The best mitigation measure

is to pre-select the site for installing the AMP at a location in sufficient distance (2-5 km) from any residential settlement.

173.           Bitumen  Works:  Such  works,  including  coat  layering  with  asphalt  concrete,  may cause a number of risks and impacts that need to be addressed in the mitigation framework. The prime risks are associated with work safety and ambient pollution. Bitumen works can also cause  health  and  safety  concerns  for  both  the  public  and  the  labourers.  Precautionary measures, being the full responsibility  of the Contractor,  include: Hot bitumen shall not get in contact with water and dust, bitumen and solvents shall not be spilled on ground, ditches or water courses. If this happens, spills need to be removed immediately and disposed in a safe site that is protected from public access. No waste material shall be burned in connection with hot bitumen. All manual works while handling bitumen require special protective clothing (shoes and gloves). Bitumen works shall not be carried out in winter, rainy or stormy weather conditions. Trucks used for hauling asphalt mixture shall be adequately equipped. Surfacing works should not occupy more than one single traffic lane at a time.

174.           Concrete Works:   Concrete is prone to become damaged  when cast at unsuitable ambient temperatures. This refers particularly to the maintenance of minimum safety standards for  road  construction  where  concrete  will  be  the  predominant  material.  Casting  concrete structures such as culverts, cattle crossings and grade separated interchange at site as well as construction of the road concrete cement surface along the road may cause spread and contamination  by  cement  dust,  which  in  turn  will  negatively  affect  soil  and  surface  water qualities. It will also result in detrimental effects on the surrounding vegetation.

175.           Mitigation  actions  include:  Restrict  concrete  works  at  site  to  suitable  weather conditions, avoiding particularly windy, icy or very hot conditions. If feasible, pre-cast solutions should  be given  preference.  Dust  development  at site  can  be managed  by suitable  covers (canvas) and/or water spraying. When casting concrete structures under water, provisions shall be  made  to  utilize  cofferdams.  Spray  waters  used  for  slowly  curing  the  new-cast  concrete structures shall not contaminate adjacent surface or groundwater resources. Proven protective methods  shall be explored  as feasible,  including  (i) collection  of excessive  spray waters and safe disposal,  (ii) covering the newly cast concrete  surface with waterproof  sheet material or sand to prevent  moisture  losses, and (iii) accelerating  the curing process  by using steam or radiant heating. While working with additives (e.g. anti-corrosive mixtures) special care needs to be  applied,  following  the  general  and  specific  precaution   prescriptions   described   in  the Contractor’s work safety guidelines.

176.          Stockpiling: Stockpiles of materials, if wrongly sited and/or protected, may cause environmental problems in terms of dust development, leaching of harmful substances into soil and  water  resources,  erosion  and  siltation.  Therefore,  stockpiles  shall  be short-termed,  and place in sheltered and guarded areas near actual construction  sites or within the camp sites. Placing shall be at minimum distances specified by the site engineer, away from sensitive areas and residential areas. Stockpiles of friable material shall be covered with clean tarpaulins, with application of sprayed water during dry and windy weather. Stockpiles of material or debris shall be  dampened  prior  to  their  movement,  unless  otherwise  specified  by  the  site  engineer. Stockpiles  shall  not  contain  any  harmful  soluble  substances,  and  be  protected  from  public access.

177.           For  each  borrow  pit  operation  site  the  contractor  shall  equally  submit  a  Site Management  Plan  including  all  planned  operations,  quantities,  hauling  arrangements  and security precautions. The plan shall provide full details on environmental  protection measures, especially in view of protecting any local water resource and proper decommissioning the sites.

F.2.7 Potential Impacts related to Waste Management and Waste Disposal

178.           Construction   works   include   transport,   handling   and   storage   of  a  number   of hazardous materials, some of them bearing critical health risks for humans, drinking water and food items when being contaminated.

179.          In this project, commendable countermeasures include: (i) development of a waste management  plan, (ii) development  of a management  plan for transport, handling and storing

hazardous material (iii) preparation of a contingency plan in the event of an accident involving hazardous material. Such emergency plan needs to be consulted and coordinated with the local health facilities. All mentioned risk management plans need to be approved by the RE and the Environmental Supervision Consultant.

180.           Explosives need be treated with specific care and arrangements  for restricted uses and  safety  measures.  The  responsibility   for  devising  management   plans  for  the  use  of explosives lies in the hands of the Contractor and will be subject to meticulous monitoring.

181.           For protection of settlements and residents, the Contractor must explore all possible means to avoid accidental spills, be it by poor transport arrangements,  by inadequate handling or  storage  of  hazardous  materials.  Such  materials  need  to  be  stored  in  special  sites  and containers  /  tanks  to  reduce  the  risk  of  accidental  spilling.  Of  special  importance  is  the observation of strict safety arrangements, i.e. storage in well-locked and fireproof areas, access restrictions  to  authorized  personnel,  all-time  watch  personnel  and  meticulous  bookkeeping records about incoming and outgoing types and quantities of such materials.

182.           Unauthorized burning of construction waste material shall be subject to penalties for the contractor, and withholding of payment.

F.2.8 Biodiversity and Ecological Resources

183.           The proposed area does not include significant habitats of wildlife and bird species. However, there is a small forest of local importance situated close to the start point of the road near the city of Shymkent and Kazygurt mountain where common species of wildlife exist. Construction works may disturb these animals and birds. Disturbance to local wildlife, such as illegal hunting activities by work forces are common problems associated with road construction projects.

184.           The EMP therefore provides a number of mitigation measures to address such likely impacts.

F.2.9 Decommissioning of Work Sites

185.           Impacts arising during the construction and decommissioning  process are temporary, generally   short-term   and  intermittent.   Nevertheless,   they  can  be  sources   of  potentially significant  effects  on  environmental    resources  and  residential  amenity,  and  states  as  an important factor in planning

186.         The EMP  makes  particular  reference  to prescribe  good  practices  for the decommissioning   of  work  sites,  both  the  construction  sites,  the  work  camp,  storage  and stockpiling facilities, and the borrow pits. To achieve proper decommissioning  of all work sites, the Contractors will be obliged to present their activities and solutions on the proper execution of such tasks as outlined in the SS EMP.

187.           The decommissioning  of work camp sites requires particular attention. Tidy clearing of all sanitary and waste management facilities, grade the soil to natural ground levels, re- establishment  of natural vegetation  and waterways  are the focal points as these are often a source  of environmental  pollution  and a public eyesore.  Options  need to be explored  which would allow the use of workers dormitories, fuel station, workshops, drainage facilities etc. for other purposes as suggested by local leaders. Good landscaping is required to re-install former work camp sites into places where the local communities would meet the desired landscape aesthetics.

F.3 Operational Phase

F.3.1 Air Pollution

188. 	Traffic-generated  air pollution is inherent to road projects, and can cause substantial health and other impacts to both the local human and biotic environment, many of them with a threatening potential for cumulative negative effects. On the other hand, the improved road conditions, less steep grades causing smaller amount of accelerations and decelerations, cause

less wear and tear to vehicles and smoother traffic flow. This will, in turn, also result in less fuel consumption and emissions.

189.           Due  to  the  anticipated  increase  in  traffic  volume,  air  pollution  along  the  road  is expected to increase. On the other hand, as only limited amount of settlements are located in close visininty to the road the magnitude of these impacts on the human health is expected to be low.

190.           To  address  potential  impacts  to  air  quality  in  this  regard,  possible  mitigation measures include:

(i) 		Setting  up  of  an  air  quality  monitoring  system  along  the  Project  Area  in accordance with acceptable standards;

(ii)        Further improvement can be made by enforcing the traffic laws and regulations to curb speeding and getting the vehicles tested, gaseous emissions, followed by mandatory technical clearance certificates;

(iii)       Strict enforcement of the regulation that no economic or settling activity takes place within the demarcated boundaries of the RoW. This refers particularly to the potential establishment of roadside vending shops and facilities.

(iv)       Should  traffic  intensity  significantly  increase,  additional  measures  might  be worth considering such as (i) enlarge and heighten the vegetation belts along the RoW in order to increase the absorptive function of roadside trees and hedges, and (ii) improving and strengthening the regional railway transport system to shift part of the cargo transport from road to rails

F.3.2 Noise Impacts

191.           Noise during operation of road is expected to raise mostly due to the (i) replacement of the surface to concrete cement and (ii) increasing the traffic volume.

192.           However,  the  impact  will  not  be  considerable  due  to  the  absence  of  any  noise sensitive  areas  located  close  to the road, feasible  effective  measures  to enforce  suggested speed limits, and planting vegetation belt between the road and settlements.

F.3.3 Hazardous Material Spills

193.           The change of the road speed and increase  of the cargo traffics will impact on a possible  risk of hazardous  material  spills that may cause long-term  negative  impacts  on the existing environment including pollution of the valuable farm lands and irrigation channels.

194.            Although the risk is extremely small since most such materials are transported  by rail, the road operator will:

(i) 	Insure that all trucks carrying  hazardous  materials  are marked  according  to

GoK norms;

(ii) 	Enforce traffic controls;

(iii)       Set speed limits for trucks carrying hazardous material to maximum 85kph or according the GoK norms and codes;

(iv)       Assist South Kazakhstan Oblast to prepare a rapid spill response and clean up protocol so that in the event of a spill the appropriate people and equipment are quickly notified and action can be taken.

F.4 Cumulative impacts

195.           Rehabilitation of the Shymkent-Tashkent  road would primarily result in wide range of cumulative impacts. However most of them will be positive and associated with socioeconomic development of the South-Kazakhstan Oblast.

196.           The proper implementation  of the EMP would minimise any impact on local human and biotic environment that might be related with any long-term cumulative negative effects.

197.           The project is planned to be implemented within ROW with no land acquisition and any impact on existing agricultural land, which suggests that cumulative land use issues would be minimized. However the proposed Project is expected to increase the local land values, especially  in the vicinity of the city of Shymkent.  Landowners  will have an opportunity  to sell their land at increased prices. Basically, this impact is estimated as a major long-term positive one that needs not be mitigated.

198.           The FS and Detailed Design indicates the implementation of the project would result in significant job creation and tax base increase and help the region retain skilled workers. Cumulative impacts on regional and local socioeconomics would therefore be positive. In some extend involvement of local businesses in international trade sector could be improved.

G. INFORMATION DISCLOSURE, CONSULTATION AND PARTICIPATION

199.           Formal Public Consultation  took place in a conference  room of the school №24 in Shymkent on the 24 May 2012, started at 15:00 pm involving about 15 participants (list of participants provided in Appendix 2). The consultation was moderated by the deputy director of South-Kazakhstan   region  Department  of  the  Road  Committee,  and  assisted  by  Designer Company (KS Engineering). The public hearings were exclusively devoted to the discussion of the potential/anticipated  environmental  impact associated with the detailed design solutions for the CAREC 3 transit corridor Shymkent-Tashkent  road Project section km 705-742 financed by the Asian Development Bank.

200.           The  Public  Consultation  was  followed  up by imitation  of some  informal  meetings carried out in Rabat, Mambetov, Aktas and Akzhar villages. The Rabat meeting took part in the building of local administration (akimat) with 11 participants. Informal consultation in Mambetov was arranged in the local point of medical service of Mambetov village collected 12 people. The Aktas meeting was limited to conversations with local dwellers living close to the Project Road. The Akzhar meeting held in the building of local administration (akimat) with 18 participants. The lists of participants provided in Appendix 2.

G.1 Preparation Works

201. 	Preparation  work started from consultative  meetings held by ADB consultants  with representatives  of state authorities  during the field survey in April and May, 2012. Important issues related to road constructions were discussed with the following agencies:

(i)  South-Kazakhstan Regional Territorial Road Department / MOTC; (ii)  South-Kazakhstan Regional Department of Environment;

(iii) South-Kazakhstan Regional Agency of Statistics:

(iv) Department  of State Sanitary  and Epidemiological  Supervision  of South-Kazakhstan

Region;

(v) South-Kazakhstan Regional Territorial Department of Forest and Hunting; (vi) Local NGOs.

202.           The following main stakeholders list was prepared based on personal consultations with above mentioned agencies:

(i)  Local   communities,   private   persons:   all   local   population,   whose   interests   are likely/potentially are affected by the planned road reconstruction and related activities;

(ii)  Government and local government bodies: Local executive agencies – Akimats of the Sairam and Kazygurt districts; Territorial  Roads Department  of the Roads Committee  of the MOTC in the South-Kazakhstan region in Shymkent; Housing and Communal Services Department in Shymkent; South-Kazakhstan Regional Department of Environment; Department  of  State  Sanitary  and  Epidemiological   Supervision  of  South-Kazakhstan Region; South-Kazakhstan Regional Territorial Department of Forest and Hunting;

(ii)   Representatives  of  the  local  civil  societies:  administrations  of  Shymkent,  Sairam, Kazygurt districts and all villages located close to the Project Road;

(iii)   Representatives   of  the  private   sector:   farm   owners;   private   companies;   local entrepreneurs.

(iv) Other institutions: local NGOs, Designer Company involved in this Project, being: KS Engineering LLC and GeoData Plus LLC.

G.2 Contacting Stakeholders and Public Announcement of the Venues

203.           The  contacting  of  the  stakeholders  being  invited  for  venues  held  in  the  Project Corridor was arranged by: Territorial Roads Departments of the Roads Committee of the MoTC in the South-Kazakhstan  region in Shymkent; Local executive agencies – Akimats of the city of Shymkent,  Sairam  and  Kazygurt  districts;  Akimats  of  Rabat,  Mambetov,  Aktas  and  Akzhar villages, Designer Companies, namely the KS Engineering LLC and GeoData LLC.

204.           Respective   announcement   on  the  planned  public  hearing  24  June  has  been published in regional newspaper “Ontystyk Kazakhstan” № 68-69 dated to 4 May 2012. This newspaper is relevant for all persons living in the respective construction corridor, and it can be obtained on all local kiosks. In addition to this personal letters of invitation were sent to all responsible state agencies and NGOs.

G.3 Performance of the Public Venue

205.           The  public  consultations   provided  detailed  information   on  the  planned  project features its foreseen activities and pre-identified environmental implications. The following methodologies were applied to accomplish the public consultation:

(i)     Speeches:           The deputy director of South-Kazakhstan region Department of the

Road Committee made an introduction to the Project Road section;

(ii)    Presentations:  Designers  presented  the  Design  Projects  of  the  road  by  using technical presentations in Microsoft PowerPoint;

(iii)   Public   Discussion:      After   presentations   all  participants   could   address   their questions and individual concerns with their own suggestions to representatives  of Local Authorities,  Territorial  Road  Department  of  the  Road  Committee  of  the  MOTC  in  the South-Kazakhstan region, Designer Company and GeoData Plus LLC.

(iv) 	Handout Information Album: All participants were supplied by Albums (A3 format) containing the mostly technical information like general Project overview; main technical features of the road; maps and summarized designer drawing solutions.

206.           Informal meeting were arranged as free discussions initiated by representative of the

RC and with active participation of Design Engineer and ADB consultants.

207.           Lists of participants and munities of the public consultation and informal meetings in hand of the Project Proponent (Road Committee of MOTC South-Kazakhstan  region). The lists of participants contain information on full names, profession and institutional affiliation, contacts and signatures (Appendix 2).

G.4 Comments Received & Response

208.           The results of public consultation and informal meetings indicates that the concerns and questions received from the side of local stakeholders related primarily to:

(i) Sourcing of construction materials

Representatives  of local NGOs asked about possible establishment of new soil reserves along the new Project Road section.

Representative  of Designer  Company  assured  that as stated in Design  documentation, there is no need of opening new soil reserves due to the fact that calculated amount of excavated ground (620.000 m3) is two times more than needed amount for filling (230.000 m3).

(ii) Distribution of information

Most of the officials participated in the PC requested a distribution of all official information on the current on going activities on the Project and shared their concerns about monitoring of the road construction.  There were also proposals  on distribution  of information  about the project,

like a summary in a hard copy which can be accessible to the public places, such as Akimat and libraries, including school.

Representative of RC announced that the final version of EMP and grievance mechanism will  be  translated   into  Kazakh  and  Russian  language  and  distributed   to  all  public information centres like akimats, local libraries and schools and RC will be involved in the monitoring process of road construction.

(iii) Cattle passages.

The  results  of  informal  meetings  with  local  residents  showed  that  there  is  no  need  in establishment of new cattle passages. However administration of the Rabat village asked to consider  possibility  of  enlargement  of  the  cattle  passage  at  km  735+700  and  to  make  it combined with agricultural machinery passage.

As  reported  by  Design  Engineer  possible  technical  changes  on  enlargement  of  the existing cattle passage at km 735+700 will be included in the final Design documentation in order to provide the open it for agricultural machineries.

(iv) Safety during the operation.

Most of the village dwellers proposed installation of waste containers, toilets and communication posts  within  new bus stops  and rest areas.  The bus stops  were asked  to be supplied  with lightning system. Integration of the fire protection measures was indicated as significant issue especially close to the Kazygurt pass. Also local drivers proposed to make Kazygurt pass more save for driving by means of the elimination  of the road incline. According  to the information given from local akimat of Rabat there are many cases of road accidents registered near the Kazygurt pass.

Representative  of Designer  Company  said  that  all  issues  will  be covered  by the  final Design documentation: all bus stops and rest areas will be supplied by toilets, waste containers and communication emergency posts and elimination of the bus stops will be introduced. Also he replied that Kazygurt pass road section is planned to be rehabilitated including decrease of the existing slope.

(v) Local communities’ utilities

People participated in the informal meetings raised their concern about possible impact on their community infrastructure, particularly water supply pipelines and power transmission lines. In addition  to  this  village  dwellers  of  Rabat  were  interested  in  technology  to  be  applied  for rehabilitation of Kazygurt pass section. They were interested in necessity of traffic diversion and bypass roads arrangement with respect to local community representatives expressed their awareness  on  possibly  considering  their  local  road  passing  through  their  community  as  a potential temporary bypass as there are vary social facilities such as school local on the road.

Design Engineer emphasized that no engineering infrastructure  will be impacted and the technology  of the rehabilitated  road construction  will be implemented  by preservation  of one part of the road in operation.

(v) Local communities’ health, possible social and economic benefits

Representative  of the  medical  station  asked  to consider  measures  to reduce  dust  pollution during  the construction  stage  due a large  number  of local  people  suffering  from  respiratory diseases (asthmatics). The local unemployed people asked if they can be employed and to be involved in construction  works. PC participant were interested in new surface of the road and the decision of construction of the concrete-cement roads.

Representative of Designer Company assured that all mitigation measures are developed in the local EIA. Decision  on replacement  of old asphalt surface to concrete  was taken based on its longer service capacities.

Representative of the RC team replied that their expectation that most of the local people will hired by Construction Company so that they can gain social benefits.

(vi) Local cultural heritage

Informal meetings’ participants  asked to assure that no damage of their local monuments  like local  visiting  sites  (Noah’s  Ark)  and  artificial  animals  and  birds.  They  also  mentioned  an importance  and  local  value  of  the  some  installations  like  memories  of  victims  of  the  road accidents.

As reported by Representative of Designer Company all construction works are planned to be implemented within ROW and no object of local value will be impacted.

(vii) Land acquisition.

Participant of PC inquired if any permanent land acquisition will be needed for the construction of the Project Road.

Official of RC No permanent land acquisition will be required for the project. (viii) Grievance mechanisms.

NGO representatives asked about the issues of potentially affected people will be solved.

RC  representative  explained  that  currently  Kazakhstan  Government  (MOTC)  is considering development and approval of new grievance mechanism with participation of local NGOs.

G.5 Planned Information Disclosure

209.          It is anticipated that in compliance with ADB's requirements for IEEs (Category B environmental analyses), the document will be provided for disclosure on the ADB website prior to Board  consideration  of the Project.  The ADB's  Environment  Policy  requires  disclosure  of Initial Environmental Examination (IEE) reports to the public.

210.           The  Contractor  will  be  contractually  obligated  to  notify  and  inform  the  public  of construction  operations  prior  to  construction  works,  publish  an  emergency  response  plan disclosing his intentions to deal with accidents and emergencies, including environmental/public health emergencies associated with hazardous material spills and similar events, etc.

211.           As  to  the  preoperational  works  done  on  the  pre-construction  design  stage,  the results of the Public Consultation and meetings will be published in a local newspaper.

H. GRIEVANCE REDRESS MECHANISM

H.1 Grievance redresses levels

212.         According  to  the  Kazakhstan  legal  and  administrative  framework  for  the implementation of Grievance Procedures is under the responsibility of local administrations (Akimats)   and   representatives   of   Project   Proponent   (RC   of   South-Kazakhstan   region). Appointive  officials  have been  designated  at these  levels  to receive,  help resolve,  report  or forward complaints received from Affected Persons (APs) and the general public. However, due to the lack of capacities at the local level (usually local villages’ akimats consist of 2 or 3 people) some affected people may still remain dissatisfied. Many grievances at local level arise due to inadequate understanding of project policies and procedures, and can be promptly resolved by properly explaining the situation to the complaining person at the site. The efforts will therefore be  to  first  seek  resolution  of  these  grievances  at  the  local  level  through  the  mediation  by Grievance Coordinators appointed at Construction Supervision Consultant and CoR, as well as by involving  designated  officials at local community,  rayon and oblast levels. In addition,  the NGOs may serve as informal mediators to facilitate grievance resolution process.

213.           The Grievance resolution process will follow the steps defined below:

(i) 	First,   complaint   resolution   will  be  attempted   at  the  level   of  Construction Supervision Consultant (CSC), which will be required to nominate a Grievance Coordinator to receive complaints, provide explanation to APs regarding their particular case, record complaints in a special forms and attempt to resolve them on spot. If the complaint can be immediately resolved Grievance Coordinator of CSC shall inform aggrieved parties about the development of their grievance and decision  made with respect to their case. If the case remains unresolved,  it is passed to the CoR for review and resolution. In addition, the APs dissatisfied with the  attention  paid  by  Grievance  Coordinator  of  CSC  may  also  refer  to  the Grievance  Coordinator  of CoR to resolve  their case. In case, the grievance  is related to serious violation of procedures / requirements or is associated with an incident,  Grievance  Coordinator  of  CSC  shall  also  immediately  notify  CoR  in written.

(ii)       At the second level, complaint resolution will be attempted at the CoR, which will also  be required  to nominate  a Grievance  Coordinator  to receive  complaints, consult with Construction Supervision Consultant and APs and will search for possibilities to resolve the complaint within one-week period. At the end of one- week period Grievance Coordinator of CoR shall inform aggrieved parties about the development of their grievance and decision made with respect to their case.

(iii)      If the complain remains unresolved after being considered at the CoR level, APs take   their   complaints   to   the   head   of   Local   Self-Government   (Akimat   of Community),  who  registers  the  complaint  and  attempts  to  resolve  it.  If  the complaint is not resolved in one-week period (with involvement of complaining parties, relevant entities and informal mediators - such as representatives of civil society / NGOs), it is passed to the Rayon Administration (Akimats of Shymkent town or Sayram, Tolebi, Kazgurt Rayons).

(iv) 	A  designated   person  in  the  Rayon  Administration   receives   the  complaint,

registers it and attempts to resolve it. If there is no resolution in two weeks, it is passed to the Oblast Administration / Committee of Roads of the MoTC.

(v)       A designated person at Oblast level / Committee of Roads of the MoTC receives the complaint and attempts to resolve it within two weeks. As part of the process of resolving the complaint the Oblast Administration / Committee of Roads of the MoTC 	must    convene    a    grievance    redress    committee    that    includes representatives of Government, professional organizations (design firm, etc.), independent partied (academic organizations, NGOs) as well as a representative of the complaining party.

(vi) 	If there is no resolution within two weeks, the case will be presented to a Kazakh

court and resolved according to Kazakh legislation, with the covenant, that for all

project related land use, social and environmental issues the specific agreements between Government of Kazakhstan and ADB will supersede national law.

H.2 Grievance Coordinators and Focal Points, Complaints Recording and Reporting

214.           In  addition  to  the  appointment  of  the  Grievance  Coordinators  of  CSC  and  CoR, Grievance  Focal Points w ill  be designated  at community,  rayon and oblast levels to receive, help to resolve, report or forward complaints received from APs and the general public.

215.           APs or other concerned individuals may visit, call or send a letter or fax to any of the Grievance Focal Points to register their comments or complaints related to land use, social and environmental  aspects of the project  (including  but not limited  to disturbance  created  to the traffic, noise, intrusion to the territory, etc).

216.           Grievance  Coordinators  of CSC and CoR,  Grievance  Focal  Points  at community, rayon and oblast levels will maintain a record-book  to register complaints,  keep track of their status. Complaint forms will be available at these entities to facilitate recording of complaints. The information of grievance resolution will be summarized in progress reports to be submitted to ADB.

H.3 Disclosure of the Grievance Process

217.          All contact details of designated officials and a clear description of the grievance mechanisms will be published in print media, distributed via brochures, posted on the MoTC website. Grievance redress mechanism  will also be presented during the public consultations and informal meetings at Project area. Association of NGOs (named “Civil council”) active in the South-Kazakhstan  Oblast can also serve as a tool to disseminate information about grievance redress  procedure  and  facilitate  awareness  rising  in  the  Project  area.  The  information  on grievance  resolution  process will also be made available at the CSC, CoR, as well as at the offices of designated officials at community, rayon and oblast levels.

I. ENVIRONMENTAL MANAGEMENT PLAN

218.           The  Environmental   Management   and  Monitoring  Plan,  presented  separately  in Appendix 3, aims to assist the local road and transport authority (MOTC and the RC of South- Kazakhstan  region) in adequately  addressing  the foreseen  adverse environmental  impacts of the Project, in enhancing the Project’s overall benefits and introducing standards of good environmental practices.

219.           To  ensure  that  the  proposed  mitigation  measures  will  be  carried  out  by  the contractors during the construction stage, the Project Proponent will undertake the following:

(i)  clearly  set  out  in  the  tender  and  contract  documents  the  contractor’s  obligation  to undertake environmental mitigation measures as specified in the Environmental Mitigation Plan in Appendix 3 (to be appended to Contract specifications);

(ii) the cost for the recommended environmental mitigation measures will, where possible, be made separate items in the Bill of Quantities. Such allocation of a separate budget for carrying out environmental mitigation measures will be crucial to assure their ultimate implementation. During procurement, contractors will be specifically encouraged to include these  costs  in their  rates  and  present  the  mitigation  cost  as a line  item  in the  Bill  of Quantities; and

(iii) explicitly require the contractor to recruit an environmental  specialist. The contractor will be responsible for the implementation of environmental mitigation measures during construction  and  shall  employ  an  environmental  specialist  who  will  supervise implementation  of the contractor’s  environmental  responsibilities  and coordinate with the RC and MOTC. The contractor, in coordination with RC (MOTC), shall set-up a grievance redress committee that will address any complaints during project implementation.  During project  implementation,  the RC shall monitor  the compliance  of the contractor  with the EMP provisions. The RC shall provide quarterly reports to MOTC and the ADB regarding the  status  of  implementation   of  mitigation   measures   by  the  contractors,   additional mitigation measures that may need to be implemented,  incidents of non-compliance  with applicable  environmental  permits,  complaints  received  from local residents,  NGOs,  etc. and how these were addressed.

220. 	It  is  proposed  that  the  construction  supervision  consultants  (CSC)  employ  an environment specialist (with civil engineering/environmental management background) to assist the environmental supervision (ESC).

221. 	During project implementation,  the MOTC (through  the RC) will report to the ADB every  month  on  the  progress  of  the  project  by  submitting  progress  report  based  on  the monitoring report submitted by the ESS/CSC and the contractor.

222.           Upon Project completion, the RC will be in charge of the operation and maintenance of the Project Road. Routine and random monitoring will be undertaken by RC district offices as scheduled in the monitoring plan.

I.1 Institutional Strengthening

223.          There is often a gap between the preparation of the EMP and incorporation of the requirements for environmental mitigation and monitoring in the contract documents. This in turn leads to a lack of proper enforcement since the objectives and procedures for attaining those objectives are not clearly stated in the contract. Therefore, it is recommended that training under the  construction  supervision  contracts  concentrates  on  raising  the  level  of  awareness  and practical skills of the RC on these aspects.

224.           The proposed Terms of Reference of the International Environment Specialist (CSC)

who will conduct the RC training and orientation for contractors is as follows:

(i) review  prevailing  government  regulations  and ADB guidelines  governing  the assessment and management of environmental impacts of road projects;

(ii)  identify  the  procedures  and  tasks  required  to  be  performed  by  RC  to  meet  the requirements of these regulations and guidelines;

(iii) review the skills of the local representatives of RC and assess the need for training to establish the capability to meet requirements for conducting environmental monitoring and implementation of mitigation measures of road projects;

(iv) prepare a short-term staff training plan and associated materials to meet immediate needs;

(v) undertake training workshops that will include the following topics:

preparation of EMPs and incorporation of associated requirements in contract documents and specifications for Consulting Services and Works contracts;

procedures for monitoring implementation including target parameters, frequency, responsibilities and means of monitoring; health and safety procedures;

(vi)  conduct  orientation/workshop  for  contractors  on  construction-related  environmental issues on road projects, implementation of mitigation measures and monitoring, and preparation of monitoring reports;

(vii) evaluate  the effectiveness  of the training measuring  improvements  in attitudes  and skills achieved through a combination of feedback questionnaires and performance evaluation; and

(viii) prepare  outline  proposals  for the longer-term  organizational  and capability development of local sub-divisions of RC in South-Kazakhstan region.

225.           The training program would typically be delivered through short classroom  training followed  by  more  intensive  on-the-job  training  site  visits  where  relevant  RC  staff  would participate directly with the international  environmental  specialist/construction  supervision staff in  reviewing   the  Contractors   submissions,   carrying   out  periodic   monitoring   inspections, attending meetings on environmental issues with the Contractor and other stakeholders, and environmental reporting.

226.           The training site visits would be timed to coincide with peak work activity in order to provide a good cross-section of monitoring activities typically including visual inspection of:

(i) discharges to watercourses; (ii) dust suppression;

(iii) exhaust emissions;

(iv) noise abatement measures; (v) protection against oil spillage;

(vi) site health and safety, sanitary facilities, etc.;

(vii) public safety, traffic management, child safety, etc.; and

(viii) documenting and dealing with public complaints.

I.2 Cost Estimates for Mitigation and Monitoring Activities

227.           The total mitigation and monitoring cost for this Project (Table -15) is estimated to be USD 1.15 million. This amount includes all mitigation, monitoring and capacity building activities, and all expenses related to environmental aspects for construction works.

228.           The cost table contains a number of additional costs that should be included in the construction budget, like dust depression, planting of trees and storage and reuse of soil. Accordingly,  these  additional  costs  are  not  included  in the  available  Design  Documentation (June 2012) made by the Design Company.

229. 	Training sessions and public campaigns are also integrated in the cost estimate and shown in detail in the Table -16.

Table -15  Environmental Cost Estimate of the Project

| No. | Activity /Item | Unit | Number of Units | Cost per Unit, US$ | Cost per Activity, US$ |
| --- | --- | --- | --- | --- | --- |
| 1. | Environmental Costs – Civil Works (included in contractor’s civil work package) |
| 1.1 | Dust suppression measures | days | 300 | 50 | 15,000 |
| 1.2 | Planting of trees | tree | 6,488 | 30 | 194,640 |
| 1.3 | Stripping of top soil and storage for reuse | m3 | 390,000 | 2 | 780,000 |
| 2. | Environmental Monitoring |
| 2.1 | Soil Tests | Soil sample | 38 x 3 | 75 | 8,550 |
| 2.2 | Air Quality Tests | point sample | 38 x 3 | 300 | 34,200 |
| 2.3 | Noise Tests | point sample | 38 x 3 | 30 | 3,420 |
| 3. | Training and Awareness |
| 3.1 | Capacity strengthening of RC staff | 4 days course | see below | see below | 6,270 |
| 3.2 | Public Campaigns, 50 person | day event | 4 days | 1.750 | 7,000 |
|  | Sub-Total US$ |  |  |  | 1,049,080 |
|  | Contingencies 10% |  |  |  | 104,908 |
|  | Total US$ |  |  |  | 1,153,988 |

Table -16  Cost Estimate for proposed Environmental Safeguard Training Activities

| No. | Activity /Item | Unit | Number of Units | Cost per Unit, US$ | Cost per Activity, US$ |
| --- | --- | --- | --- | --- | --- |
| 1. | Remuneration of EC | days | 6 | 400 | 2,400 |
| 2. | Per diem of EC | days | 6 | 50 | 300 |
| 3. | Local travel and accommodation of EC | days | 5 | 80 | 400 |
| 4. | Local Interpreter | days | 6 | 100 | 600 |
| 5. | Field visits | days | 2 | 500 | 1,000 |
| 6. | Preparation of training materials, Certificates and Reporting | lump sum |  | 1,000 | 1,000 |
|  | Sub-Total US$ |  |  |  | 5,700 |
|  | Contingencies (ca 10%) |  |  |  | 570 |
|  | Total US$ |  |  |  | 6,270 |

J. CONCLUSIONS AND RECOMMENDATIONS

230.           The Project will have some negative and positive environmental impacts on physical, ecological and socio-economic environment during road construction and operation phases. As there  are  no  environmentally  sensitive  areas  in  the  Project  Area,  no  substantial  negative ecological  impacts  are warranted.  The road corridor  already  exists  and this is an upgrading project. Temporary environmental impacts are anticipated during construction; they will be minimized by proper planning, good engineering design and implementation of the proposed mitigation measures and monitoring programs and will not pose any threat to the environment.

231.           The  project  is  classified  as  Category  B  and  as  implementated   environmental assessment shows, the project likely to have no significant effects on the existing environment. Due to this fact no additional environmental examinations or development of EIA is required.

232.           The  total  environmental  cost  estimate  makes  the  sum  of  USD  1.16  million  that equals to 0.9 % of the total project cost.

233.           An   Environmental   Management   and   Monitoring   Plans   have   been   prepared, describing mitigative measures and monitoring actions to be undertaken during the pre- construction, construction and operating phases of the project.

234.           The following recommendations are proposed based on the findings of the IEE:

(i) 	Environmental Provisions in Bidding and Contract documents. The Environmental Management and Environmental Monitoring Plans, which are part of the IEE, should be a part of the Bidding documents. The Bidding documents set out that the Contractor will be responsible for the implementation of the EMP through his Site Specific Environmental Management Plan that will be based on the EMP, and will incorporate site specific details that are not presently known. The EMP should then be added to the Contractors Contract, thereby making implementation of the EMP a legal requirement. Specific environmental provisions covered by EMP related but not limited to:

(a) 	erosion control, air and water quality control,

(b) 	location of asphalt plants, construction  camps and other facilities (not in environmentally sensitive areas indicated above),

(c) 	borrow pit restoration, (d) 	quarry operations,

(e) 	safety provisions,

(f) 	baseline   and   routine   monitoring   of   noise   and   vibration   levels   in settlements;

(g) 	baseline   and   routine   monitoring   of   air   quality,   water   quality,   and ecosystem health, and

(h) 	community relations;

(ii)          Environmental  Monitoring and Control. Baseline air quality and noise monitoring is  recommended   in  the   city   of   Shymkent,   Aktas   and   Mambetov   villages   at   the preconstruction  stage as well as consideration of the relevant mitigation measures during detailed design.

(iii)          Capacity   Building   for  Environmental   Management.   A  training   program   for selected staff of the PIU and addressed to the goals and techniques of environmental management activities in road projects is strongly recommended.

Typical  cross  sections of the road

Type 1 with  embankment up to 1 meter

Type 1 with  embankment up to 3 meters, whith separated roadways of different directions

Type 1 with  embankment up to 3 meters,

Typical cross sections of the road

Type 4 with excavation up to 2 meters

Type 1 with excavation more than 2 meters

Type 1 with embankment up to 3 meters,

The cross  section of the cattle passage combined with agricultural machinery passage

The design of the rehabilitated road pavement

CnucoK  yqa Cl HHKOB KOHCYJ ibTau.uu  no npoeKTY  . JI)'I.JtueHue 1	P3C Kopu.r.opa, ( WbtMKeHT	a rnKeHT)

(lllbiMKCHT-TarnKeHT) IJ,AP3C-Ti._ 3 AaJibi "'ocnapbl 60Mb1HlUa KeJt :ecy K.3Tb1CYlllbiJiap ri '31Mi

(?0

fO 	a.m. , June6, 2012 	, 0 HIOHSI  2012 r0)1;3

6 MayCbiM 2012 JK.

Name, Surname

<1>. H.O.

A.T.)J(.

Contact details  (phone, e-mail ) KouTaKTHble .[{aHHble (TeJl. JJl. a.[{pec) liaHJI3HbiC aK:na  aT  (TeJI., JJI. MeKeH-iK3Hbt)

Signature

IJO.[{OHCb

1\0Jlbl

ol .

«··

't. Y-.'-<	;/.c  a.u. eMc-

u/1.	,, 	v(f	/

-'"1 .S::- E>S. ll'29

a.(  \At.@_ s',wo ot -'. c..o

ff   ?<!-  --1-j  ::J  3 	6 &

/Y'J C4l 	@  11(/-?PI  b Ier. ,.v

C nuco K y "-laCTHHKOB KOHC:VJJ hTauuu  no uooe KTY YJJY'-tmeHu e LI,AP3C KO pll.i iOpa 3 (WhiMKeH T- TamKeHT) ( WhiMKeHT-TamKeHT) LI,AP3C-T tl-( 3 llaJJili IKOcnaphl 60Hh1Hma Ke3Llecy aThlcymhiJJap TiliMi

K /1.Cl.fl-the...-frrv  /ln , June 6, 2012 	-   ft11,6 HIOHH 2012  ro a

/<	JD

v 	/ 		MaychiM 2012JK.

-	1 6

1

J.,	0

3 .

Name, Surname

<f). H.O.

A.T.JK.

w(

6 ee	\I.a...Q.UA. "'

Contact details  (phone, e-mail ) KoHTaKTHble J],aHHhle (TeJJ. JJJ. aJ], pec)

6aHJI3HbiC aK;na  aT  (TCJI.,JJI. MCKCH-iK3Hbl)

Signature lloJ], nHcb

1\0JJbl

6 	vir

J.

-

1	Ia

/c? 	k 	.--/ 	A

//.

/L

1) 	List  of Participants of the  Consultations for  CAREC Corridor 3 (Shymkent- Tashkent) Improvement Project

CnncoK yqacTHHKOB KOHCYJJbTaunu no npoeKry YJJylfmeHne  IJ,AP3C Kopn.z:.opa 3 (UlMMKeHT- TamKeHT)

(lllMMKeHT-TamKeHT) .QAP3C-Ti--. 3 .U JJi3i mocnapbl 6onMHma Ke3_uecy l(aTMcymMJJap ThiMi

o-0

AtUtr  I 5 J>!l1 , JuneS, 2012

I

--' 6 HIOHH 2012 ro_ua	 		6 MaycMM 2012 m.

Name, Surname

<1>. 11.0.

A.T.JK.

I

Contact details (phone, e-mail ) KonTaKTnLieannLie (TeJI. JJI. a pec)

6ai1naHbiC a na aT   Ten., 3n. MeKeH->KaMbl

Signature llo  nucb

1\0Jibl

4

;f . 	7 <?¥-& ....£'	fl?e.

£	-6d

/r	/

c/'	»--:!Z

ua.	..-fo.-

).if-MA'I	'fffrt·4 1-'

------------ ----

/L.

List  of Participants of the 	onsultations  for·CAREC	on·idor·3 (Shymkent- Tashkent) Improvement Project CnHcoK  yqacTHHKOB KoncyJlLTau,Hn no npoeKry YJlyqwenue U,AP3C KOpH)l.opa 3 (lUbiMKeHT- TawKeHT) (lllbiMKeHT-Taw KenT) II,AP3C-Ti.._ 3 )l,aJli3i ocnapbl 6oiiLrnwa Ke3)l.ecy aTMcywLrJlap TiliMi

l:..z..ar	/So-e  , June' 2012 	, 6 HIOHH 2012 rO)l,a	6 MaycMM 2012

.N'!!	Name,  Surname 	Contact details (phone, e-mail ) 	Signature

<1>.  u.o. 	KonTaKTHhle [laHHhte (TeJJ. 3JJ. a[lpec) 	llO[lDHCh

A.T.)K. 	6al1naHbiC al(na  ar  ren., Jn. MeKeH->KaHbl	1\0JJbl

IJ	eudo	vf . vf 	eX!// -eX' 1- sr:r	/'

C!	vf. 	q	'7--f .

1)	;u. 	(1\    C-h'

It	!(_	d	fYrlAA  ?b/b

17-	v£1: /f)- 	{)? 	? 7f:r./--t>.r!J

li	6Q	e . o 	1) t:.L7-;;_ 	v £AJ-

L ist of Participants of the  Con. t  ltations for  CAREC Corridor 3 ·  h · mke nt- Tashkent) Improve  1 ·n &      P roject C nucoK  yqacTHHKOB KOHCYJI L 1 a un it no npoeKTY Y nyqmeHue U	·.:)	Kopu,nopa  3 (WhiMKeHT- lamKe HT) (WbtMKeHT-TamKeHT) 	AP3C-Ti.._ 3 ,nani3i ocnapbt 6oubmma KeJ,necy "aTbtcymhtJiap Ti3iMi

(

4-f' v:;	/3 	,June 6, 2012

.N'!!	Name, Surname 	Occupation 	Contact details (phone, e-mail ) 	Signature

<1>. H.O.	MecTo  pa6oTM 	KouTaKTHMeaHHLie (TCJI. 3JI.  a pec) 	fio nHCL A.T.)K. 	 )KyMLIC OPHLI	  6aHJJ3HbiC aK:napaT (TeJJ.,JJI. MCKCH- aHbl) 		f\OJJLI

/	'!:t?

rtJ )ta

...L1 J...   .A. t ,1..<--	I

d1-

2:	!'

:J:-o. r !f) z""c; /L )l l  ;, K.	; ·f 0 j 9 s"-! j- .%1 lJ:; l :f c !,/;.}.77 r4

L	)r ,  t 11 (!._ i ,r"J	r

fc,

U	V/	I 	If'

J/

)J . (

.i U  I  cl I b	(._f. LiLC!	K

3	. ·r._ a. .-t_ .).f/-J}1 £/i. 1JV., I	/ 	.h(,(_....

!?1....C:!-A.t::.

.;fac

I

o/;:;Jza.

1	--; ?Vrf' ..

0:...

/Jol

!A	/ urn u-efA'	t1<'? n ., 152 376 b

tf.-:-

r? 	/-

c:

etz.. /}

-=.:-- 	£a,c·Z7..-Y/"	· 	/

0//:/;;  / '7/

/)1 .., 4 (c..l?....;k...   t"-er:p A

...,/

f	;; 	-s ., f 	!/./ 	t/ f'

l> -

c 	p;lt cpA	)-p; 	J2?D .s-?2.2 ;;<; 71 	7_

<1:::  -	/

- -

\

(lllbiMKeHT-Tam KenT) l.J,AP3C-Til( 3 Jl3Jli3iuil( ocnapbl 6olihiHWa oFaMJlblThiH.llay.llhll(aTbiCYWbiJJap.llbll( TiliMi List of Participants of the Public Consultation for CAREC Corridor 3 (Shymkent-Tashkent) Improvement Project CnucoK  yqacTHHKOB o6mecTBeHHbJX cnywauuu no npoetrry YJJJ'IWeHHH U,AP3C Kopn.llopa 3 (lllbiMKeHT-Taw KenT)

| 0. )l(aH.nocos Keweci,NQ 24 MeKTe | 0. Zhandosov str. school N!!24 | yn. 0. )l(aH.nocosa, JJ.. NQ24, WK NQ 24 |
| --- | --- | --- |
| lllbiMKeiiTaJlaCbl, 24 MaMblp 2012 | Shy mkent, May 24, 2012 | lllbiMKeHT, 24 MaH 2012 rOlla, |

A.T.JK. 	liaiiJJallbiC al(napaT 	JKblllbiCbl	TlfpFbiJi bll(fbl iKepi	JK¥Mb1C OpHbl	JlaybllbiMbi 	I(OJ1bl

N!!	Name, Surname	(Tell., Jll. MeKeH-)1(8H bi)	(E >Kie 8)	MecTo 11\IITeJJbCTBa	Occupation	)J.OJDKHOCTb	Signature

<)).U.O.	Contact details 	OoJJ (M 11 )J()	Residence 	MecTo pa6oTbl 	Position 	nolliiHCb

(phone, e-mail ) 	Gender

KonTaKTIIbJe llaHHbJe	(M & F)

(Tell. Jll.aupec)

1

-1.

f	/r

tt:r

1-W	a e-r.	cJ'y

......,.

TJ r--

Uw .vut	1:;-o" //j-6J	t-	t2,t; IUftbP	, ,. I .

v vv "'(J-''k-!PtulaU. 	tr 	tr 	j

"fvLJ,t{  l.CJ..//..<)//]

_; -9

5 -	6'1.-.	l/ off    jJ u

LL dGa

Y:c.r-

c;:;

(fL<J

:ZOJ

,c.

)lt<-

w".J'l .u.t. ·

Jhl V, 0 p ,

..t.l

t:r.{_

1:1 r A  GD

'Cr.., kY tc"D 	.

{)Lt;  :.t.e._

ft:2L

_q	/.::>

1

clk  c -Y 	,_(?j'yy6"_5  /U'O

_y t *

J--' /p('£;••'

(	'--·7 W/7C7·1  (.

1¢/

c.?(·

TSS" ;;;	/-	/-:c	.

7-<- Yc'c..:..;

.	' er -.J	.

J

rr 	JI      u. il.tL  I

_,.7	-1 '-

..>f-ltl t 4 	dru

-- 	t. /' f '

-AGP	   -

-

A

t UrJ-Lr  ...1-t:. 	.I

-r-

-	'::>

c [u sv..t	c.J{I

d 	t'-11 l' c.-	(_  l.. 	rL 	rJt.tfJ a. (/

, 	.A. - tC

co-- :i'rf":'llt.M..t ...s... 	,((...l'• "c• r r  rt r \Lf•    lL<• ft tt• lt>#c,. ;

"

s	'J.

.< .._r _  (

- ·-J j-rY 	o

4	ytN,_ kil 9Jc-._,:-  4.-t. / f 	/ ;{//"·

I	'2 	( ].j	,   p

6	c£...- 	1

,.,/ /."•t-::;:-e,	t:Ji"? -1f!)S'/( C"	'1•«.(	L"'-1 .. 	,. 	4 ,? uu r 	42.-	A	. c_

t (t..  c;:.u .<- 	.4z-.n 	{/'/•?"'

.;.	t-o(	f! 	6-.lei r"29 05 c.,(	-rc.	t:!c u .,.(".t(	-z.

fi.u.,.(  l'C .

..	.---G .. ?	rc.-c,y,	7	C-< N .,,c.;::•<.Cf'

:1 i!?:f//

- -• - -a -•  ---- _ 	..	.-	-

-  - • a    • - -

-- 	-

-- • -r

t-<".. 1..   c: u ,:_

- -·- 	-·-

----------

(lllbiMKeHT-TamKeHT) I(AP3C-Titl 3 )l3JJiJiHitl  iKOCnapbl 60HbiHWa OFaM)lblTbiHJlay)lbltlaTbiCYWbiJJap)lbltl TiJiMi

List  of Participants of the Public Consultation for CAREC Corridor 3 (Shymkent-Tashkent) Improvement Project

CnncoK yqacTHHKOB o6mecrseHHbiX cJJymauuii no npoeKTY YJiyqmeunH U:AP3C KOpHAOpa 3 (lllbiMKeHT-TamKeHT)

0. )l{aHJJ.OCOB Keweci, NQ 24 MeKTe 	0. Zhandosov str. school NQ24	yn. 0. )l{aHJJ.ocosa,JJ..  NQ24, liiK NQ 24

lllbiMKeHTaJJaCbl, 24 MaMblp 2012 iK. 	Shymkent, May  24, 2012 	lllbiMKeHT, 24 MaH 2012 ro)la,

A.T.)K. 	liaiinanbtC aR;napaT	)KblllbiCbl 	T¥pFbiJibiKTbl iKCpi	1biC Opllbl JiaybiJbtMbt	]\OJibl

.N2 	Name, Surname	(Ten., :m. MeKeH-)l(aHbi)	(E >K/e 8) 	Mecro il\ltTCJibCTBa	Occupation	)1.OJiil\11OCTb 	Signature

.11.0.	Contact details 	Don (M H )I{) 	Residence 	Mecro pa60Tbt	Position 	DOllnJICb

(phone,e-maiI)	Gender

KOHTaKTIIbte llallllble	(M& F)

(Ten.3n.a.npec)

'j	h

/..6-J 0-.1-1 	c:ul-	g-1 o , 	·z f 'L'L Lf  o	M	K(lrl'?- r-t fl_•  .1..	fi(fj	/if  k 'K	{;

K-	.l.tf'.-ty;-'i.s>	{f 	l.f '2	J_LCl..l..t...e;,.../.1

9	c{.,;:Ou c; l Jl'o,rv	f! ?o2  ..::,p9(..Y 01.( 	/'1 	2	p/,_.d (ru ;	tfd· I';u... ".

- J_a .t

n

(·--/

(. "

D  c-<det.,	c.?.tj.>l"

.l;ya

d'i

)o?..c.:>9  (/ 	.

It 	;f v.u.._r-:J a	1.   ttu, <-tL  "''-''	Jf.l t(.C C[)K  A cp 	'1.A    C.!(.	if

1-f;JrY(J 1rbfei\..Q (..

8 1--oI	5 	r tl i	M 	c Ill ,....,	9 s-..5	MT.,..k Pte	na r..	M

.-	ul'l,	.u.-f't'

"

v  'l .........   t

/4 U•Qif

f	U eL....t.t £e.- c..(; 	f-C fc 0 t7:)J:; 177;)	.

Ql1j'

(I 	_

,.	9. "+ on  6 8, (:,' ..t 	5

1,-u...,  .r cr,._,o.,. urz	"'

14	,A-II tJ K /),k

.o 	C./J <:5

09-u  /o:>-.0

I';

t CJt o<f.C  &(,;	2 	/t ,,u,u .'

/J

c.·:.·, 	#)

l),.,,u,f 	J, ( VI <· IS' .I f  1" 	..1./	(/,;.A.

I t f..C<.  ( 	L

1'01CO . J }l  ,.1£	!fer

t l t Ct -	'

/I u.

U, 	Jury ,,l.o;	tl	,MtTu  ft   /I(

/5	f t .. 1'f£(.'f 	c <-	:/77f!-rcf f tr T.Jc

-t;!

t..'C.{6{._(,K.'CL/	/<; 	.1ft' /( r 	r:	. 	?,,-

.JC.. (	Y·.	&<.

Pt dj•	t/! "d y..<c ' 	L

l,jJ"J"  . 	.!/ICC	/c £.	t /'ill;'	t.'/

/ · 	,l 1' l

/

r

.....     ---·- ... 	___ -------·.....	.... ..... -·-- 	--- -----.. ...	__ ., _      _ -·-----------	-- ·- __._        ___

.....__

-	.-- -··--

Appendix 3

Environmental Management Plan:

PART  A. 	Mitigation Measures for Identified Potential Impacts

A.1 	PRE-CONSTRUCTION   PHASE

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.1.1 Bid documents prepared without access to or use of the IEE and particularly this EMP in a translated version | No bid documents will be prepared without the authors having incorporated a (Kazakh/Russian) copy of the mitigation and monitoring plan EMP, which shall be included in the safeguard clauses of the Technical Specifications in the contracts. | Shymkent, availability of documents at RC | Before bid documen ts are complete d | Detailed Design Consultant and RC | MOTC and PMU with advice from MOEP | included in the Project Costs |
| --- | --- | --- | --- | --- | --- | --- |
| A.1.2 Poor landscape aesthetics due to Design | Consider aesthetical roadside plantations as much as environmental conditions (e.g. water supply and availability of plants) allow | Near existing grade separated interchange at km 732+963 | at early design stage | Detailed Design Consultant | MOTC and RC | included in the Project Costs |
| A.1.3 Site selection for large construction camps, near or within existing settlements. Impact on public health and sociological setting | Proper site selection, observing criteria which primarily protect the public general. Observe a minimum distance (buffer zone) between camp site and nearest residential area. Observe local wind conditions to reduce nuisances. Work safety and environmental protection measures to be specified by the Contractor in a Site Management Plan (SS EMP). Planning for independent water and electric supply network and a medical service station at the site. | At selected camp site locations, wherever these are in close vicinity to settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | at early design stage | Designer | MOTC and RC | included in the Project Costs |
| A.1.4 Planning for structure demolishing and removal of utilities for widening the RoW | Provide for adequate and safe removal of demolished structures in certified dump sites. Plan for timely and fully functional substitution for any public utility that needs to be removed. Obtain certificates from local authorities. | At all locations where utilities need to be removed and substituted | at early design stage | Detailed Design Consultant | Local Authorities responsible for utilities | included in the Project Costs |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.1.5 Road safety issues associated with pedestrian crossing | Planning for safe and adequate pedestrian crossing facilities that can be in most cases over passages equipped with ramps and structures that allow the use of wheelchairs, pushcarts, bicycles and prams. Planning for public awareness meetings | Near all close located settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov), bus stops and rehabilitated grade separated interchange | at early design stage shortly before works start | Detailed Design Consultant | MOTC and RC | included in the Project Costs |
| --- | --- | --- | --- | --- | --- | --- |
| A.1.6 Road Accidents with livestock animals | Planning for suitable protective measures, as 1. Pre-consult with local people, to identify spots where mitigation measures are needed 2. Plan for animal (under-)passages, sufficiently dimensioned, taking into account specific behavioural aspects to allow safe use by different livestock species 3. Plan for strong animal fences along each side of an animal passage 4. Provide adequate length and strength of animal fences along the two established /planned protected areas | At 4 locations of existing cattle passages combined with agricultural machinery passages | Before the bid documents are completed | Detailed Design team – following field inspection and stakeholder consultation, and in consultation with the Environmental Department Units in Shymkent | MOTC and MOE, and CHF | included in the Project Costs / Civil Works |

A.2 	CONSTRUCTION   PHASE

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |
| A.2.1 Contractor fails to retain a ecological expert to prepare the SS EMP and to implement all mitigation and monitoring measures as specified in the EMP | As specified by law, contractor will be required to employ a licensed expert to prepare the SS EMP and obtain all relevant permits. The contractor will not be permitted to mobilize workers without an approved SS EMP and the appropriate permits in place. | Entire road section for which the SS EMP will be prepared | Prior to the start of the construction work. | Contractor | MOTC and PMU, Environmental Supervision Engineer | to be included in the Project Costs |
| A.2.2 Common issues related to operation of camp sites (environmental, social, security, public health, workers safety, sanitary, and waste concerns) | The contractor will be required to employ a licensed expert to prepare the SS EMP which will address all potential impacts identified in the IEE. Focal aspects are medical care, insurances, social welfare, work safety, good housekeeping practices, work hours, security, crime prevention, electricity and water supply, waste management, awareness training, grievance relief. | - as above - | - as above - | Contractor | MOTC and PMU, Environmental Supervision Engineer | to be included in the Project Costs |
| A.2.3 Large water extraction volumes for construction purposes and camps may lead to conflicts with local water users | Contractor/sub-Contractors must submit a plan for type, location and quantity of both drinking and technical water extraction. The plan needs to be approved and monitored by the responsible authorities. Prevent any illegal fishing in local rivers which would involve labourers. | At all locations where water extraction is planned (possible source is Badam river) | Throughout construction works. | Contractor (and all sub- contractors) | Local Water Authorities, RE, Environmental Supervision Engineer | to be included in the Project Costs |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.2.4 Contractor undertakes excessive, unauthorized or unnecessary tree removal or causes damages to ecologically vital vegetation at construction sites | The contractor is required to develop a sketch map of the location number and species of trees along the roadside that he intends to cut. Such plan needs to be screened by the Supervision Consultant and approved by the RE. The Contractor must develop a plan for replacing any removed tree or important vegetation, and engage the CHF in the intended replanting scheme, describing: species selection, minimum size, number of young trees per cut tree, maintenance for a specified time, replacement of unsuccessful replantation | Along any section of the road were trees are subject to the Contractor’s discretion for removal | Prior to any clearing taking place | Contractor, with advice from the Oblast CHF | PMU, Environmental Supervision Engineer | to be included in the Project Costs / Civil Works |
| --- | --- | --- | --- | --- | --- | --- |
| A.2.5 Sourcing of materials; Side borrow operations leading possibly to erosion, landslide and landscape deterioration. Impacts associated with stockpiling | Materials may only be excavated in authorized borrow pits. Contractors shall develop a borrow pit site management plan to ensure all precautions for avoiding environmental impacts. While not strictly forbidden, the practice of taking fill material from the side of the road, creating a landscape of craters shall not be acceptable unless complete landscaping and erosion control follows. Any such borrow areas should not intrude visually on the road, meaning it should be out of eyesight from the road with proper site re- contouring and replacement of topsoil. Provide adequate fencing to prevent unauthorized access to borrow sites. Provide for proper decommissioning plan for each borrow site. | At all rehabilitation sections where additional material is required from borrow pits; impact zones requiring special protection include the hauling roads. | Throughout the construction period | Contractor | MOTC and PMU, RE, Environmental Supervision Engineer | to be included in the Project Costs / Civil Works |
| A.2.6 Potential Impacts associated with the Asphalt Mixing Plant (AMP) | Choose operation site for AMP (as for crushers) at least 2 km away from the next human settlement, and always on leeward side with respect to prevailing winds. | At all construction sites nearby settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | Throughout the construction period | Contractor | RE, Environmental Supervision Engineer | included in the Project Costs |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.2.7 Potential impacts associated with bitumen works | Avoid, all time, contact of bitumen with water and dust; Bitumen and solvents shall not be spilled on ground, ditches or water courses. If this happens, spills need to be removed immediately and disposed in a safe site that is protected from public access. No waste material shall be burned in connection with hot bitumen. All manual works while handling bitumen require special protective clothing (shoes and gloves). Bitumen works shall not be carried out in winter, rainy or stormy weather conditions. Trucks used for hauling asphalt mixture shall be adequately equipped. Surfacing works should not occupy more than one single traffic lane at a time. | At all construction sites | Throughout the construction period | Contractor | RE, Environmental Supervision Engineer | included in the Project Costs |
| --- | --- | --- | --- | --- | --- | --- |
| A.2.8 Potential Impacts associated with concrete works | Avoid concrete works during windy, icy or very hot conditions. Aim at pre-cast solutions. Dust development at site can be managed by suitable covers (canvas) and/or water spraying. While working in streams casting concrete structures utilize cofferdams. Use spray waters for slowly curing and make all precautions to avoid contamination of adjacent surface or groundwater resources. Cover newly cast concrete surface with waterproof sheet material or sand to prevent moisture losses, and accelerate the curing process by using steam or radiant heating. While working with additives (e.g. anti-corrosive mixtures) special care needs to be applied, following the general and specific precaution prescriptions described in the Contractor’s work safety guidelines. | At all construction sites | Throughout the construction period | Contractor | RE, Environmental Supervision Engineer | included in the Project Costs |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.2.9 Improper management of earthworks; transport and storage procedures, impacts caused by any activity generating dust and air pollution | Large volumes of quarry rock, aggregate and sand will be transported and stored to work site. Hauling roads (dirt roads) need regular water spraying to contain dust development. 1. Ensuring that the contractor’s fleet of vehicles and diesel generators are properly maintained and tuned to prevent excessive pollution; inspection reports are submitted to the RE 2. Observance and control of specified haul loads; as and if necessary, upgrade the haul roads into all-weather road; 3. Documentation that the Contractor uses specified fuel for his fleet; 4. Use of dust suppressants (regular watering) 5. Vehicle operators must make provisions to cover trucks, particularly during windy conditions. 5. Truck and excavator operators must strictly observe specified speed limits being 30 km/hr near (100 m) or within settlements. 4. Vehicle idling time must not exceed 2 min. All topsoil needs to be collected, stored in appropriate stacks, protected from wind and rain, and be fully re-used to rehabilitate/revegetate the areas disturbed and as specified by the RE. | Anywhere where material is excavated and transported to/from sites of construction | Throughout the construction period | Contractor (being responsible for local sub- contractors) | MOTC and PMU / RE, Environmental Supervision Engineer | to be included in the Project Costs / Civil Works |
| --- | --- | --- | --- | --- | --- | --- |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.2.10 Improper management of petroleum products such as fuel, lubricants and bitumen, leading to spill and contamination. | The Contractor/Sub-contractor will be required to have the following spill prevention measures in place at all work sites: 1. All fuelling to be done on a concrete surface pro- voided with spill catch tank that can be cleaned and all spilled fuel recovered and recycled based on discussions with fuel supplier. 2. All repair and maintenance work must either be done on a concrete surface with oil spill catch basin or oil catch pans must be provided at all service areas and training provided to all mechanics. 3. All fuel use areas where spills and leakage is possible, e.g. the generator, must have drip basins installed to pre-vent leakage. All recovered materials must be recycled. 4. A fuelling areas must be equipped with proper fuel nozzles and means for preventing accidental spills. 5. All bitumen handling must not permit any material from leaking to the ground, including transfer areas and any areas where bitumen is transported in drums. 6. Bitumen drums must be stored in a dry covered secure place where no leakage to water or ground is possible. Drums must be recycled at least once/yr. 7. Any spills must be cleaned up according to GoK norms and standards within 24 hours of the occurrence, with contaminated soils and water treated according to GoK norms and standards. Records must be handed over without delay to the RE. | At all construction sites, and within camps and storage facilities established | Throughout construction works, including decommissio ning phase. | Contractor (and all sub- contractors) | MOTC and PMU, RE, Environmental Supervision Engineer | to be included in the Project Costs / Civil Works |
| --- | --- | --- | --- | --- | --- | --- |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.2.11 Noise and vibration impacts, generated by construction activities, leading to health impacts and damages to structures | Contractor shall take all necessary steps to: 1.Selection of modern and well-serviced equipment and plants with reduced noise level ensured by suitable in-built techniques and appropriate silencing devices; .2.Confining excessively noisy work and movement of heavy machinery to specified daytime working hours (this relates especially to stone crushers. percussion hammers and pneumatic drills); 3. Work hours need observe special restrictions near residential and sensitive areas; 4. Providing the construction workers with suitable hearing protection (ear muffs); 5. Avoid vehicle idling. 6. Timely public announcements of works | At all construction sites, especially those located nearby settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | Throughout the construction period | Contractor | MOTC and PMU, RE, Environmental Supervision Engineer | to be included in the Project Costs / Civil Works |
| --- | --- | --- | --- | --- | --- | --- |
| A.2.12 Failure to adhere to construction related good housekeeping practices, including solid and sanitary waste management | Contractors will adhere to standard good house-keeping practices as defined in the contract Terms & Conditions and Contract Specifications: 1. Management of construction waste and water 2. Equipment lubricants and fuel, including management and collection of waste oils and fuel particularly related to refuelling depots, maintenance areas and diesel generator sets 3. Sewage will require latrines or chemical toilets with complete clean up after the construction is complete. 4. Garbage will be collected and properly disposed, in accordance with GOK norms and codes 5. The contractor shall orient all construction workers and on the specific hazards of their work and will need to certify to that effect at the start of the construction period. 6. Once the site is no longer needed the contractor must fully decommission it, with emphasis on waste removal /clean up of any spills or hazardous materials plus any necessary revegetation. | All work camps, construction maintenanc e yards and any other areas operated by the contractor and involved in the project | Throughout the construction period | Contractor (including sub- contractors) | MOTC and PMU | to be included in the Project Costs / Civil Works |

A.3 	OPERATION 	PHASE

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.3.1 General traffic safety | Appropriate road signage, traffic monitoring and control, human capacity development, review of the driving license issuing system and a wise application of penalties seem to be the most likely responses. The installation of an early warning electronic and radio system in case of bad road conditions ahead may also considerably contribute to improve the road safety. Evaluate the introduction of publicly accessible, well- marked posts containing both an emergency (pay-free) telephone and a first-aid box with medical supplies, stretchers, bandages and other means for first assistance to road victims. To avoid misuses, these boxes shall be equipped with an electronic lock that can only be opened by prior telephone contacting to a nearby police station. | Emergency phone posts at bus stop/ rest areas and in the vicinity of the Kazygurt pass. | at the start of operations | RC, in collaboration with local Traffic police and local medical services | MOTC and Traffic Police | t.b.d. |
| --- | --- | --- | --- | --- | --- | --- |
| A.3.2 Increased risk of pedestrian accidents within settlement areas due to improved roads, faster speeds and greater traffic volume | To manage these problems the operator will enforce speed limits through increased ‘radar’ surveillance, better and more frequent signage and increased speeding fines. In villages at crossing the owner will improve the signage and include amber lights were possible. As many town bypasses as possible are planned and should reduce project generated traffic through towns and villages. | Close to the close located settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov)and grade separated interchange | at the start of operations , at defined schedule | RC, in collaboration with local Traffic police and Environmental Agencies | MOTC and MOE | t.b.d. |
| A.3.3 Inadequate management of traffic-generated air pollution | Adequate signage and awareness measures forwarded by Traffic Police, to improve the flow of traffic, reduce deceleration- acceleration cycles and idling periods, all measures that will lead to the overall reduction in the emission levels, despite the predicted increase in the overall traffic volume. Consider air pollution test program. | Where applicable and required, nearby human settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | t.b.d. | RC, in collaboration with Environmental Agencies | MOTC | MOTC |

| Environmental Impact/ Issue | Mitigation Measures | Location | Time Frame | Responsibility | Costs / Budget |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Implementation | Supervision |  |

| A.3.4 Traffic-related noise development, affecting nearby human settlements. | Identify feasible and effective measures to enforce suggested speed limits. Within settlement areas, where soil and soil humidity conditions would allow, consider the establishment of natural noise barriers (hedges), based on a specific monitoring program | Before and after Kazygurt pass and all close located settling areas (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | t.b.d. | RC, in collaboration with Environmental Agencies | MOTC | MOTC |
| --- | --- | --- | --- | --- | --- | --- |
| A.3.5 Increased risk of hazardous material spills due to increased traffic volume and provision of larger capacity bridges and stronger road surfaces, inviting large trucks to use the road. | Although the risk is extremely small since most such materials are transported by rail, the road operator will: 1. Insure that all trucks carrying hazardous materials are marked according to GoK norms 2. Enforce traffic controls 3. Set speed limits for trucks carrying hazardous material to max. 85kph or according the GoK norms and codes. 4. Assist South Kazakhstan region to prepare a rapid spill response and clean up protocol so that in the event of a spill the appropriate people and equipment are quickly notified and action can be taken. | Close to the close located settlements (especially Shymkent, Aktas, Akzhar, Rabat, Mambetov) | Within the first year of the road being in operation | Road Operator, Traffic Police MOTC to arrange for District Contingency Plan | MOTC and MOE | MOTC |
| A.3.6 Potential spread of STDs and human trafficking | Commendable actions to curtail such impacts are: 1. Public awareness campaigns to address risks associated with human trafficking; 2. Increased controls on highway sections where girl traffickers are reported to operate 3. Seeking assistance of locally operating NGOs. | Especially in the Shymkent, Aktas, Akzhar, Rabat, Mambetov | Continual activity, as required by records of incidences | SES, Traffic Police | SES | SES own budget |

Environmental Management Plan

PART  B:   Environmental Monitoring

| B.1 PRE-CONSTRUCTION PERIOD |
| --- |
| Monitoring Aspect | Monitoring Activity / Details / Outputs | Timing | Executing Unit | Reporting Responsibility |
| B.1.1 No provision for translation of IEE and related documents for use by Oblast Inspectors, and for use in Bid documents ( at least this EMP) | Confirm that Kazakh/Russian version of IEE and EMP are with the Oblast Inspectors Confirm that bid documents contain environmental clauses tailored to the project conditions as well as a copy of the precautionary measures outlined in this EMP | During Detailed Design Period, at the time of preparing the bid documents | MOTC/ RC | MOTC |
| B.1.2 Failure of designers to include design measures that will prevent later impacts such as: livestock crossing management, poor traffic management and excessive tree removal | Confirm by reviewing design documents and discussion with design team that 1. livestock crossings in Section 3 have been addressed 2. a plan to protect roadside trees as much as possible has been prepared; 3. there is step-by-step protocol for traffic management during construction ( as opposed to ad hoc, hap hazard existing system); and 4. an environmentally friendly bridge and culvert replacement guide has been prepared | During Detailed Design Period, at the time of preparing the bid documents | Detailed Design Team under the direction of MOTC/ RC | MOTC |
| B.1.3 Lack of capacity to understand and implement environmental mitigation measures, in particular the compliance monitoring procedure | Collect and review written material and expertise indicating that MOTC has provided instructions for the contractors to use to better use the IEE output Prepare environmental compliance forms together with Contractors and Sub-Contractors to secure acceptance | During Detailed Design Period, at the time of contract awards | Environmen tal Supervision Engineer MOTC/ RC | MOTC |

| B.2 CONSTRUCTION PERIOD |
| --- |
| Monitoring Aspect | Monitoring Activity / Details / Outputs | Timing | Executing Unit | Reporting Responsibility |
| B.2.1 Availability of ecological expertise to prepare the SS EMP and to implement all mitigation and monitoring measures with contractor | Confirm ecological expertise is with contractor at start of construction period: check CV and license certificate(s). Discuss with contractors/sub-contractors the management implications of all measures included in EMP. | At time of each contractor appointment | PMU | MOTC |
| B.2.2 Lack of good housekeeping practices at both camp sites and work sites, including solid and sanitary waste management | Using agreed monitoring checklists, confirm that the items as listed in the SS EMP and in the Technical Specifications are fully implemented. | Throughout construction period, monthly | PMU | PMU and MOTC |
| B.2.3 Tree removal program damaging the old trees and shelter belt plantings along roadsides kept to an absolute minimum. | Inspection of cutting plan and confirmation of consultation with CFH, then review and record re-planting/revegetation efforts. | Throughout the construction period, spot checks | PMU Monitor with the CFH of the Oblast and Rayon were cutting is foreseen | PMU and MOTC |
| B.2.4 Side borrow operations leading to erosion, landslide and destruction of landscape | Undertake inspections to determine the type of borrow operations the contractor is applying and ensure that roadside borrowing is not taking place and is always out of the visual field from the road. | Throughout the construction period and monthly | PMU | PMU and MOTC |
| B.2.5 Earthworks - transport and storage; managing of dust, noise | Undertake, as part of the construction inspection, regular confirmation that earthworks are handled in an environmentally acceptable manner and dust control is undertaken at all time, including the use of tarpaulins by trucks hauling fine materials, as well as watering along the haul road sections passing near/thru villages, and that a speed has to be decreased. Haulage through roadside villages and settlements is restricted. | Every day, throughout the construction period | PMU | PMU and MOTC |

| Monitoring Aspect | Monitoring Activity / Details / Outputs | Timing | Executing Unit | Reporting Responsibility |
| --- | --- | --- | --- | --- |
| B.2.6 Potential bitumen/asphalt and concrete production spills and pollution. | Confirm that sighting specification for both asphalt and concrete plants are according to norms and codes but also that are at least as far away from settlement areas as defined in the mitigation table. Bitumen storage and handling is done without spillage | Throughout construction period and monthly | PMU | PMU and MOTC |
| B.2.7 Management of petroleum products such as fuel, lubricants and bitumen, without spills and contamination being practiced by contractor and all subcontractors. | Using the monitoring checklist the 8 specific spill of Mitigation table will be assessed and reported on. Unannounced (spot) inspections at all work sites, work camps. diesel generators, technical workshops, maintenance yards and fuel storage facilities. Any non-compliance will be rectified immediately | Quarterly inspections, unannounced | PMU Monitor | PMU and MOTC |
| B.2.8 Potential deficiencies of surface drainage at construction areas | The PMU will inspect and verify that adequate consideration and drainage works and protection have been provided. | 4X during the construction period, and 2X during each rainy season | PMU | PMU and MOTC |
| B.2.9 Construction-related air pollution | Using a monitoring checklist confirm that the six mitigate actions defined in A.2.9 of the Mitigation Table are being implemented | Ongoing throughout the project as part of the construction inspection | PMU | PMU and MOTC |

| B.3 OPERATION PERIOD |
| --- |
| Monitoring Aspect | Monitoring Activity / Details / Outputs | Timing | Executing Unit | Reporting Responsibili ty |
| B.3.1 Post construction operational audit, 1-year after road completion | The owner of the road shall organize and undertake a complete environmental audit of the project. This audit is to be undertaken by the Oblast-level DOEP. Findings must be reported within 15 days of completion of the field inspection and actions to repair any non-compliance conditions started within 5 days of notification by the Inspection Department. All actions must be completed within 30 days. | No more than 13 months after the operating period has fully started. | MOTC, and MOEP | MOTC and Oblast-level Department of Env. Inspection Unit. |
| B.3.2 Management of traffic- generated air pollution | As traffic growth is projected to reach 7%/year, a site-specific monitoring at roadside settlements will be required. Parameters to be monitored are in line with the norms and codes of the national environmental legislation. Monitoring Report. | Monitoring 1X/year for two continuous 24 hour period during the non- winter season at t.b.d. sites | MOTC in cooperation with KAZHYDRO- MET or other approved agency | MOTC |
| B.3.3 Management of traffic- generated noise | Noise impacts are expected to marginally affect human settlements due to the remoteness. Near or at settlements (bypasses) noise levels need to be tested to confirm or modify the measures taken. Parameters to be monitored are in line with the norms and codes of the national environmental legislation. Monitoring Report. | Monitoring will take place 1X/year during peak traffic periods over two 24 hour monitoring periods at t.b.d. sites | MOTC in cooperation with Ministry of Health’s Sanitary and Epidemiologi cal Service | MOTC |
| B.3.4 Risk of road accidents with pedestrians and domestic animals due to improved roads, faster speeds and greater traffic volume. | Report on the effectiveness of proposed measures for pedestrian and animal crossing structures, and make further recommendations to improve road safety with respect to these aspects. Modify, as applicable, speed limit signage, pedestrian use zones, and provide more cross walk lighting. Reconsider, as necessary, strengthening and extension of animal fences along road. Accident Monitoring Report. | Undertake annual safety check and review statistics of pedestrian- vehicle accidents and address areas where problems occur | MOTC working with Oblast and Rayon level authorities | MOTC |

| Monitoring Aspect | Monitoring Activity / Details / Outputs | Timing | Executing Unit | Reporting Responsibili ty |
| --- | --- | --- | --- | --- |
| B.3.5 Risk of hazardous materials spills due to increased traffic volume | Elaboration of a contingency plan in case of major emergencies, and plan responsibilities for different scenarios. | after one year of operation | MOTC working with Oblast and Rayon level authorities | MOTC |

Abbreviations used in the EMP:

SS EMP -	Site-specific Environmental Management Plan

CFH	-	Committee for Forestry and Hunting, under the Ministry of Agriculture

GoK	-	Government of Kazakhstan

MOEP   -	Ministry of Environmental Protection

MOTC   -	Ministry of Transport and Communication

PMU	-	Projects Management Unit, Team of consultants working closely with the Implementing Agency, the South-Kazakhstan region Road Committee (RC) RC	-	(South-Kazakhstan) Road Committee, under the MOTC

RE	-	Resident Engineer

SES	-	Sanitary and Epidemiological Services, under the Ministry of Health t.b.d.	-	to be determined